## Slide 1: Test framework for LTM cell switch
Issue 5-2-1: Procedures and configurations of test cases on cell switch delay
3GPP TSG-RAN WG4 Meeting # 110bis R4-2406497
Changsha, China, April 15 – 19, 2024

## Slide 2: Issue 5-2-1: Procedures and configurations of test cases on cell switch delay
Tentative agreement - Ad-hod
  For test case for cell switch in the following table, introduce T1~T5:
    T1: at starting point of T1, UE has no timing info of target cell. UE is configured with L3 and L1 measurement for cell 2. UE is given time to perform L3 for cell 2. T1 ends when TE receives L3 measurement report.
    T2: TE provides LTM configuration. Ends when TE recevies L1 RSRP report.
    T3: TE triggers TCI activation (only for UE supporting early TCI activation)
    T4: TE triggers RACH. (only for RACH-less cell switch and for UE supporting early timing acquisition)
    T5: TE triggers cell switch. Verify cell switch requirements during T5.
  Power level of target cell remains the same starting from T1.
  Timeline can be revisited based on conclusion of other open issues.

## Slide 3: Issue 5-2-1: Procedures and configurations of test cases on cell switch delay
UE capability | Early TCI | Early PRACH | LTM CS | FR | Intra-freq PCell | Inter-freq PCell | Intra-freq PSCell
Type 1 | Yes | Yes | RACH-less | FR1-FR1 | A.6.3.x.4 |  | 
Type 2 | No |  |  |  | A.6.3.x.3 |  | 
Type 3 | Yes | No | RACH-based |  | A.6.3.x.2 | A.6.3.x.6 | A.6.3.y.2
Type 4 | No |  |  |  | A.6.3.x.1 | A.6.3.x.5 | A.6.3.y.1
Type 1 | Yes | Yes | RACH-less | FR2-FR2 | A.7.3.x.2 |  | 
Type 2 | No |  |  |  | A.7.3.x.2 |  | 
Type 3 | Yes | No | RACH-based |  | A.7.3.x.1 | A.7.3.x.3 | A.6.3.y.3
Type 4 | No |  |  |  | A.7.3.x.1 | A.7.3.x.3 | A.6.3.y.3
To be merged
To be merged
To be merged
To be merged
UE capability types:
Type 1: UE capable of ‘early TCI state activation’ and ‘early PRACH’
Type 2: UE capable of ‘early PRACH’ only
Type 3: UE capable of ‘early TCI state activation’ only
Type 4: UE incapable of ‘early TCI state activation’ and ‘early PRACH’

## Slide 4: Issue 5-2-1: Procedures and configurations of test cases on cell switch delay
Type 1: UE capable of ‘early TCI state activation’ and ‘early PRACH’
Cell 1
(source cell)
Cell 2
(target cell)
Connection establishment and L3 MO config.
TE turns on the power of cell 1
UE establishes a connection with the cell 1
TE turns on the power of cell 2
Cell 1 provide L3 measurement configuration for cell 2
UE report L3 result of cell 2 to cell 1
T1
Tx power X dBm
Tx power X+Y dBm
L3 measurement report
LTM configuration
L1 measurement report
T2
T3 ([10] ms)
Cell 1 configures LTM-Config and CSI-MeasConfig for cell 2
UE reports L1 result of cell 2
TCI state activation
Cell 1 sends ‘Candidate Cell TCI States Activation’ MAC CE
Note: Joint or separate TCI states depending on UE capability
PDCCH-order
Cell 1 sends PDCCH-order
UE tx’es PRACH to cell 2
PRACH
Single SSB
Single SSB
LTM cell switch command
T4
Contention-free PRACH
RACH-based:
  UE tx’es CF-PRACH
RACH-less:
  TE continuously tx’es UL grant
  UE tx’es PUSCH with RRCReconfigurationComplete
PUSCH
RACH-based
RACH-less
UL grant
T5
Reset

## Slide 5: Issue 5-2-1: Procedures and configurations of test cases on cell switch delay
Type 2: UE capable of ‘early PRACH’ only
Cell 1
(source cell)
Cell 2
(target cell)
Connection establishment and L3 MO config.
TE turns on the power of cell 1
UE establishes a connection with the cell 1
TE turns on the power of cell 2
Cell 1 provide L3 measurement configuration for cell 2
UE report L3 result of cell 2 to cell 1
T1
Tx power X dBm
Tx power X+Y dBm
L3 measurement report
LTM configuration
L1 measurement report
T2
T3 ([10] ms)
Cell 1 configures LTM-Config and CSI-MeasConfig for cell 2
UE reports L1 result of cell 2
TCI state activation
Cell 1 sends ‘Candidate Cell TCI States Activation’ MAC CE
Note: Joint or separate TCI states depending on UE capability
PDCCH-order
Cell 1 sends PDCCH-order
UE tx’es PRACH to cell 2
PRACH
Single SSB
Single SSB
LTM cell switch command
T3
Contention-free PRACH
RACH-based:
  UE tx’es CF-PRACH
RACH-less:
  TE continuously tx’es UL grant
  UE tx’es PUSCH with RRCReconfigurationComplete
PUSCH
RACH-based
RACH-less
UL grant
T4
skip
Reset

## Slide 6: Issue 5-2-1: Procedures and configurations of test cases on cell switch delay
Type 3: UE capable of ‘early TCI state activation’ only
Cell 1
(source cell)
Cell 2
(target cell)
Connection establishment and L3 MO config.
TE turns on the power of cell 1
UE establishes a connection with the cell 1
TE turns on the power of cell 2
Cell 1 provide L3 measurement configuration for cell 2
UE report L3 result of cell 2 to cell 1
T1
Tx power X dBm
Tx power X+Y dBm
L3 measurement report
LTM configuration
L1 measurement report
T2
T3 ([10] ms)
Cell 1 configures LTM-Config and CSI-MeasConfig for cell 2
UE reports L1 result of cell 2
TCI state activation
Cell 1 sends ‘Candidate Cell TCI States Activation’ MAC CE
Note: Joint or separate TCI states depending on UE capability
PDCCH-order
Cell 1 sends PDCCH-order
UE tx’es PRACH to cell 2
PRACH
Single SSB
Single SSB
LTM cell switch command
T4
Contention-free PRACH
RACH-based:
  UE tx’es CF-PRACH
RACH-less:
  TE continuously tx’es UL grant
  UE tx’es PUSCH with RRCReconfigurationComplete
PUSCH
RACH-based
RACH-less
UL grant
T4
skip
Reset

## Slide 7: Issue 5-2-1: Procedures and configurations of test cases on cell switch delay
Type 4: UE incapable of ‘early TCI state activation’ and ‘early PRACH’
Cell 1
(source cell)
Cell 2
(target cell)
Connection establishment and L3 MO config.
TE turns on the power of cell 1
UE establishes a connection with the cell 1
TE turns on the power of cell 2
Cell 1 provide L3 measurement configuration for cell 2
UE report L3 result of cell 2 to cell 1
T1
Tx power X dBm
Tx power X+Y dBm
L3 measurement report
LTM configuration
L1 measurement report
T2
T3 ([10] ms)
Cell 1 configures LTM-Config and CSI-MeasConfig for cell 2
UE reports L1 result of cell 2
TCI state activation
Cell 1 sends ‘Candidate Cell TCI States Activation’ MAC CE
Note: Joint or separate TCI states depending on UE capability
PDCCH-order
Cell 1 sends PDCCH-order
UE tx’es PRACH to cell 2
PRACH
Single SSB
Single SSB
LTM cell switch command
T4
Contention-free PRACH
RACH-based:
  UE tx’es CF-PRACH
RACH-less:
  TE continuously tx’es UL grant
  UE tx’es PUSCH with RRCReconfigurationComplete
PUSCH
RACH-based
RACH-less
UL grant
T3
skip
Reset