## Slide 1: Fragmented spectrum scenarios
For information
Source: TELUS, Bell Mobility, Telstra

## Slide 2: Canadian operating bands
Canadian bands are aligned with the following licensed terrestrial NR bands:
n2/n25, n5, n7, n12, n13, n29, n30, n38, n66, n71, n77/n78
The following bands are fragmented (FDD bands and TDD bands):
n25, n7, n66, n77/n78
The focus of the currently proposed study item is on 3 FDD bands:
n7, n25, n66

## Slide 3: Applicable CC blocks across three FDD bands
Band | CC 1 |  | CC 2 |  | Comment
 | DL range (MHz) | UL range (MHz) | DL range (MHz) | UL range (MHz) | 
n7 | 2620 - 2640 | 2500 - 2520 | 2670 - 2690 | 2550 - 2570 | Main markets
 | 2620 - 2630 | 2500 - 2510 | 2660 - 2690 | 2540 - 2570 | Other markets
n25 | 1945 - 1970 | 1865 - 1890 | 1980 - 1995 | 1900 - 1915 | Biggest market
 | 1945 - 1970 | 1865 - 1890 | 1985 - 1995 | 1905 - 1915 | Second biggest
n66 | 2140 - 2155 | 1740 - 1755 | 2170 – 2200* | 1770 – 1780* | Major markets
 | 2135 - 2155 | 1735 - 1755 | 2170 – 2180 | 1770 – 1780 | Many other markets
*Asymmetric DL/UL

## Slide 4: Applicable CA combos
CA combos submitted so far were limited by the CC count, where n77(3A) dominates the CC count
DL CA combo | Typical CC Bandwidths | Comment
CA_n7A-n25A-n66A-n77(3A) | 20-25-30-60-100-40 | 6 CC combo submitted in March 2024
CA_n7(2A)-n25(2A)-n66(2A)-n77(3A) | 20-20-25-15-30-15-60-100-40 | Target 9 CC combination would add 50 MHz (added bandwidths in red)

## Slide 5: Australian operating bands
Australian bands are aligned with the following licensed terrestrial NR bands:
n1, n5/26, n3, n7, n8, n28, n78
The following bands are fragmented (FDD bands and TDD bands):
n1, n26, n78
The focus of the currently proposed study item is on 1 FDD band:
n26

## Slide 6: Key FDD band of interest for Australia
Band | CC 1 |  | CC 2 |  | Comment
 | DL range (MHz) | UL range (MHz) | DL range (MHz) | UL range (MHz) | 
n26* | 860 - 870 | 815 - 825 | 880 - 890 | 835 - 845 | Main markets (metro)
 | 860 - 870 | 815 - 825 | 875 - 890 | 830 - 845 | Other markets (rural)
*Asymmetric DL/UL

## Slide 7: Applicable CA combo for Australia
CA combo has a mix of 2Rx (n26) and 4Rx (n7 & n78)
DL CA combo | Typical CC Bandwidths | Comment
CA_n26(2A)-n7A-n78(2A) | 10-15-40-60-80 | 5 CC combo approved in March 2023