## Slide 1: Way forward on UE Transmit Timing Accuracy Test in DRX (Re: R4-132715[1] & R4-132718[2] referring to Clause 7.1 & A.7.1 of TS36.133)
FUJITSU
R4-133022
TSG RAN WG4 meeting #67
Fukuoka, Japan, 20 - 24 May, 2013
[1] R4-132715, “UE Transmit Timing Accuracy Test in DRX (Discussion paper)”, Fujitsu.
[2] R4-132718, “UE Transmit Timing Accuracy Test in DRX” (Corresponding CR), Fujitsu.

## Slide 2: The gist of the argument in R4-132715
  For ‘The initial transmission (timing requirements) in a DRX cycle for PUCCH, PUSCH and SRS or the PRACH transmission’ requirements in TS36.133;
  Only the timing error limit (Te) is defined in clause 7.1. [Te=12Ts(=391ns)*1]
  No MAMTOA*2 requirement is set for DRX case, while for Non-DRX case, both MAMTOA & MATAR*3 are set as Tq/occasion & Tq/200ms respectively. [Tq=3.5Ts(=114ns)*1]
  ‘Test 2’ in A.7.1 insists UEs to capture the artificial timing shift in the DL of 64Ts (=2us) with DRX start offset & DRX cycle of 80ms . [UE speed@350km/h causes timing shift of only 26ns/80ms. 2us corresponds to 40% of a normal CP]
  The consequence would be: A UE compliant to ‘Test 2’ could easily miss-detect DL timing when in DRX and follow erroneous timing in DL (the timing error could be larger than 2us as there is no MTOA requirements) [especially for eg., in heterogeneous cell environment. Once it happens, the UE may need long time to return to its genuine Tx timing.*4]
    *1: For 10MHz BW case as an example
    *2: The maximum amount of the magnitude of the timing change in one adjustment
    *3: The Maximum Aggregated Timing Adjustment Rate.
    *4: Not explicitly stated in R4-132715.

## Slide 3: Points discussed in R4#67 (either in online or offline)
  For ‘The initial transmission (timing requirements) in a DRX cycle for PUCCH, PUSCH and SRS or the PRACH transmission’;
  The timing accuracy requirements in clause 7.1 should not be changed (especially for frozen releases eg.Rel-8.)
  In case changes are needed to the test conditions in A.7.1, it should be applied up to Rel-8 to keep consistency. The change should not (cannot) affect the existing UEs.
Way forward
Fujitsu to provide further analysis of the area and may propose a resolution based on the analysis at R4#67.
In the mean time, companies are encouraged to review the above findings or discussions from the online/offline discussions in R4#67 and provide their view at R4#68.