## Slide 1: Way Forward on RS-SINR
Qualcomm Incorporated, AT&T, Vzw, CMCC
R4-134484
3GPP TSG-RAN WG4 Meeting # 68
Barcelona, Spain, 19th – 23rd August, 2013

## Slide 2: Way Forward
RS-SINR for the serving cell is widely used as a metric to set the antenna bar display in many devices
  RS-SINR is currently not standardized and different devices can have different performance.
Interested companies are to check the feasibility of introducing RS-SINR for the serving cell in the specifications(see proposed definition on next page) and defining accuracy requirements and a performance test until RAN4 #68bis meeting
  Other use cases(e.g. eMDT) could also be analyzed

## Slide 3: RS-SINR proposed definition
RS-SINR is defined as the linear average over the power contribution (in W) of the resource element carrying CRS divided by the sum of the noise and interference power contribution (in W) of the resource element carrying CRS within the considered measurement frequency bandwidth. For RS_SINR determination, the cell-specific reference signals R0 according TS 36.211 shall be used. If the UE can reliably detect that R1 is available it may use R1 in addition to R0 to determine RS-SNR.
The reference point for the RS-SINR shall be the antenna connector of the UE.
If receiver diversity is in use by the UE, the reported value shall not be lower than the corresponding RS-SINR of any of the individual diversity branches