## Slide 1: WF on Interruptions to E-UTRA due to D2D operation
Qualcomm Incorporated
R4-146661
3GPP TSG-RAN WG4 Meeting #72bis
Singapore, Oct. 6th – Oct. 10th, 2014

## Slide 2: Background
For D2D on TDD bands, no interruptions to E-UTRA required due to D2D
  No receiver re-tuning
  D2D Rx on UL subframe is similar to Rx on any DL subframe
For D2D on FDD bands, interruptions to E-UTRA required due to D2D
  Communications
    Two receiver chains are assumed
    Interruption due to turning ON/OFF of D2D Rx chain (same as Scell add/release)
    UE indicates ‘start’ and ‘stop’ of interest in D2D, corresponding to turn ON/OFF of receiver chain
    Note: only 2 subframes during entire D2D operation
  Discovery
    Single or two receiver chains are possible
    Additional interruption due to re-turning (DL to/from UL) receiver chain before and after a D2D subframe
    Note: interruption location known at eNB. Infrequent due to low duty cycle of discovery.

## Slide 3: Way Forward
UE allowed to interrupt PCell and SCell(s) UL and DL on 1 subframe during the RRC reconfiguration procedure that includes the configuration message proseDiscConfig or proseCommConfig
    For discovery, UE is allowed to interrupt PCell and SCell(s) UL and DL on 1 subframe immediately before and after a D2D subframe