## Slide 1: Way forward on CA performance requirements applicability
Qualcomm, Ericsson
3GPP TSG RAN WG4 #72bis
Singapore, 6th – 10th October 2014
R4-146810

## Slide 2: Background
CA performance requirements in chapter 8/9 are band agnostic
  Band specific UE performance are verified by RF receiver test defined in chapter 7
  band agnostic CA performance requirements are supposed to be verified in one CA configuration
  CA test applicability rules are clarified in RAN4 #72 (R4-145422)
  Some operators have concern for CA performance requirements test coverage
CA capability column in CA performance tests
  CA capability column was specified from Rel-10 and has been maintained up to now
  There is a concern from some companies that CA capability column is not useful but is causing confusion in RAN5

## Slide 3: Way forward
CA applicability
  For 2 DL CC, following CA capabilities are tested
    Inter-band CA
    Intra-band contiguous CA
    Intra-band non-contiguous CA
  CA capability for 3 DL CC is FFS
  For CA TM3 demodulation test, tests will be applied to one CA configuration from each CA capability supported by UE
  For other CA performance tests, tests will be applied to one CA configuration from one CA capability supported by UE. Tests include
    Normal demodulation test TM1, TM4
    Soft buffer tests
    Sustained data rate test
    CQI tests
  Applicability rule in section 8.1.2.2 will be revised to capture the agreements in RAN4 #73

## Slide 4: Way forward
CA capability column in CA performance tests
  Companies that want to keep/remove CA capability column to provide analysis on the benefit of keeping/removing it
  Analysis could include
    Information provided by CA capability column
    Implication of CA capability column on RAN5 work
    CA capability column for 3 DL CA
  Analysis on other aspects are not precluded