## Slide 1: WF on layer 3 and 4 demodulation requirements
Huawei, Hisilicon
R4-154238
TSG RAN WG4 meeting #76
Beijing, China, 24-8 Aug, 2015
Agenda Item: 7.8.4.1

## Slide 2: Way forward
Test cases will be introduced for layer 3 and 4 demodulation requirements in R.13 4RX WI
  TM3
  TM4
  TM9
Test purpose is to verify the UE’s implementation at least on the following aspects
  MIMO receiver
  layer-to-codeword mapping
  Channel estimation and rate-matching of DMRS port 9/10 for DMRS-based transmission
  Layer3/4 precoding vector for TM3/4/9

## Slide 3: Assumptions
The following table is information for simulation alignment, companies are encourage to bring more analysis and evaluation
Transmission mode | TM3 | TM4 | TM4
Bandwidth | 10MHz |  | 
Scheduled PRB | 50PRB |  | 
CCH symbol | 2 |  | 
Antenna configuration | 4x4 low |  | 
Propagation channel | EVA70 | EPA5 | EVA70/EPA5
CRS configuration | Port 0,1,2,3 | Port 0,1,2,3 | Port 0,1
DMRS configuration | - | - | Port 7,8,9,10
CSI-RS configuration | - | - | Port 15,16,17,18
scheduled subband | [1 2 3 4 6 7 8 9] |  | 
Overhead | 23.8% | 23.8% | 38.1% and 35.7% *
CSI feedback | PUCCH 1-0 | PUCCH 1-1 | PUCCH 1-1
Beamforming model | - | Followed wideband PMI | Followed wideband PMI
Layer number | Option 1: Layer 3; Option 2: Layer 4 |  | 
MCS | Option 1: MCS14; Option 2: Others |  | 
* The overhead are different for subframes with/without CSI-RS