## Slide 1: Draft WF on Retuning Time of Rel-13 MTC UE
Qualcomm, Sony, Ericsson, Nokia Networks, Huawei, Verizon, Intel, Sequans, NTT Docomo, Alcatel-Lucent, Alcatel-Lucent Shanghai Bell
R4-154846
3GPP TSG RAN WG4 Meeting #76
Beijing, China, 24th - 28th August 2015
Agenda item 7.7.1

## Slide 2: Background
RAN4#75 agreement:
  Proposed retuning time between narrowband regions for MTC varies between 76µs and 350µs.
  RAN4 is to investigate until the next meeting (RAN4#76) to agree on one value for the retuning time.

## Slide 3: Proposal
The maximum retuning time between narrowband regions for MTC is 2 symbols including CP length (assuming normal CP)
RAN4 requirements if defined will be based on the maximum retuning time mentioned above
NOTE: some UEs may be able to perform retuning within a single symbol (including normal CP)
  Note: RAN4 discussion is applicable only to RF re-tuning time