## Slide 1: WF on CRS-IM PDSCH demodulation
Ericsson, ZTE
R4-155191
3GPP TSG-RAN WG4 Meeting #76
Beijing,China, Aug 23~Aug 28, 2015

## Slide 2: CRS-assistance information
Reuse “CRS-AssistanceInfo-r11” as required assistance information (triggering signaling) for CRS-IM. RAN2 could discuss the extension to Scell if needed.
CRS-IC can be applied to all subframes.

## Slide 3: UE Capability
Option 1: Not define new UE capability signaling and reuse the R.11 crs-InterfHandle signaling to imply the R.13 CRS-IM capability
Option 2: Define new UE capability signaling including information on the number of supported CCs for R.13 CRS-IM UE.
Option 3: Define new UE capability signaling indicating CRS-IM support on at least one serving cell
Companies are encouraged to provide more inputs for this issue in the next meeting

## Slide 4: Requirements applicability
RAN4 requirements are defined only for non-CA case.

## Slide 5: Gain test case list
Introduce the following test cases for the gain test:
  CRS-based transmission scheme (TM2 and/or TM4)
  TM9
  TM10

## Slide 6: For robustness test
Option 1: There is no robustness test
Option 2: Introduce TM3 for robustness test
Companies are encouraged to provide input for this robustness test

## Slide 7: Serving cell MCS for non-TM10 (Gain test)
Collect simulation results in this meeting and make tentative MCS selection based on the results

## Slide 8: About the requirements for non-TM10 (gain test)
Option 1: Companies can provide both 1-cell CRS-IC and 2-cell CRS-IC results for alignment and decided the requirements based on the aligned results
Option 2: Defined performance requirements based on 1-cell CRS-IC
Other options are not precluded

## Slide 9: Test setup for TM10
For one CSI-process capability UE
  PDSCH scheduling: PDSCH is static scheduled from non-serving TP within CoMP set
For multiple CSI-process capability UE
  Option 1: PDSCH is static scheduled from non-serving TP within CoMP set
  Option 2: DPS, i.e., TP for PDSCH transmission is dynamically changed between two TPs within CoMP set
Interference modelling for the TP within the CoMP set
  Blanking
Interference modelling for the TP outside the CoMP set
  Partial load with lower RU 20%
Transmission mode for the TPs
  TM10/TM10/TM9
  Note: TP1, 2 is within COMP set and TP3 is outside COMP set

## Slide 10: Interference profile for TM 10 test on one-CSI-process capability UE
For the aggressor cell within the CoMP set, the interference level is [10.45] dB
For the aggressor cell outside the CoMP set, the interference level is:
  Option 1: [8.45] dB
  Option 2: [6.45] dB
Companies are encouraged to provide inputs on these options in the next meeting

## Slide 11: Interference profile for TM 10 test on multiple-CSI-process capability UE
Companies are provide input on the interference profile for TM10 test on Multiple-CSI-process capability UE.