## Slide 1: Way forward on coexistence simulations results for in-band and guard band
Huawei, Ericsson, Intel, Nokia Networks, ZTE…
3GPP TSG-RAN WG4 Meeting #78bis R4-162806 San Jose del Cabo, Mexico, 11 – 15 April, 2016

## Slide 2: Background
The power leakage modeling data with same granularity from different companies are not totally same (e.g. with/without filtering).
The simulation results from different companies are based on their own power leakage model.
Companies provide their power leakage model and simulation results into R4-162805 for comparison.

## Slide 3: Coexistence results
For NB-IoT aggressor,
  Adjacent LTE PRB level (both for in-band and guard band)
    Average throughput loss in range of percentage,
      1st PRB ~[2.1%, 17%], 2nd PRB ~[0.3%, 3.3%], 3rd PRB ~[0%, 1.6%], other PRB ~[0%, 0.2%]
    5%-ile throughput loss in range of percentage,
      1st PRB ~[0.6%, 47%], 2nd PRB ~[0, 4.5%], 3rd PRB ~[0%, 1.1%], other PRB ~[0%, 0.1%]
    Average SNR loss in range of dB
      1st PRB ~[0.15, 1.61], 2nd PRB ~[0.01, 0.2], 3rd PRB ~[0, 0.1], other PRB ~[0, 0.03]
    5%-ile SNR loss in range of dB
      1st PRB ~[0.03, 3.1], 2nd PRB ~[0, 0.2], 3rd PRB ~[0, 0.1], other PRB ~[0, 0.02]

## Slide 4: Coexistence results (cont.)
For NB-IoT victim,
  In-band
    5%-ile SNR loss in range of dB ~[0.15, 5.6]
    50%-ile SNR loss in range of dB ~[0.3, 1.5]
    95%-ile SNR loss in range of dB ~[0.72, 1.9]
    99%-ile SNR loss in range of dB ~[0.7, 2.1]
  Guard band
    5%-ile SNR loss in range of dB ~[0.12, 2.9]
    50%-ile SNR loss in range of dB ~[0.2, 0.9]
    95%-ile SNR loss in range of dB ~[0.4, 2.1]
    99%-ile SNR loss in range of dB ~[0.4, 2.2]

## Slide 5: Way forward
Power leakage model is somehow dependent on implementation (e.g. filtering), sinc-shaped pulse filter could be regarded as the worst case. Comment: Not sure this difference could really explain all results’ differences: we all have similar power leakage, but still, simulations results are not converging.
NB-IoT can coexist with LTE in-band and guard band with the observations as follows,
  NB-IoT perform some interference on 1st adjacent LTE PRB, while the interference on other PRBs is insignificant or acceptable.
  Some impact on NB-IoT at high SNR.
  Guard band operation perform slightly better coexistence compared to in-band operation.

## Slide 6: References
R4-162805, “Summary of coexistence simulation results for in-band and guard band”, Huawei, Ericsson, Intel, Nokia Networks, ZTE.
R4-162311, “UL coexistence simulation results for in-band operation”, Huawei
R4-162312, “UL coexistence simulation results for guard band operation”, Huawei
R4-162097, “Coexistence evaluation for in band and guard band”, Ericsson
R4-161811, “Simulation results of coexistence studies between NB-IoT and LTE, in-band case”, Intel
R4-161812, “Simulation results of coexistence studies between NB-IoT and LTE, guard-band case”, Intel
R4-162643, “Further discussion on power leakage model for NB-IOT in-band/guard band”, Nokia Networks
R4-162804, “Simulation results of co-existence study of NB-IOT in-band/guard band operations”, Nokia Networks
R4-161941, “Summary of power leakage level between LTE and NB-IoT”, ZTE
R4-161942, “Updated simulation results for in-band scenario”, ZTE
R4-161943, “Updated simulation results for guard band scenario”, ZTE