## Slide 1: Way forward on UE performance requirements for FD-MIMO
Samsung, Qualcomm, Intel, [Ericsson]
3GPP TSG-RAN WG4 Meeting #80
Gothenburg, Sweden, 22 - 26 Aug, 2016
R4-165941

## Slide 2
  DMRS configuration for target UE
  Fixed as port 11, nSCID=0, OCC=4
Number of interference port
  1 port with nSCID= 0,OCC =4
Interference port selection: randomized interference port between port{7, 8,13}
  Option 1: per TTI per RBG basis
  Option 2: per TTI per RB basis
  Option 3: per TTI basis
  Decide set-up in next RAN4 meeting
Detailed test parameters
  Reusing existing test parameters for FRC, propagation channel, antenna correlation, and beam-forming mode as specified in 36.101 8.3.1.1 Test 2
Performance requirements:
  Bring simulation results and deciding performance requirements for FDD mode and TDD mode in next RAN4 meeting.
PDSCH demodulation test(RAN4#79 agreement)

## Slide 3
Interference port selection: randomized interference port between port{7, 8,13}
  Defining test case with test setup as per TTI per PRG basis
  The minimum performance requirements are based the assumption interference port detection and interference covariance matrix estimation per RB basis
  FFS if test setup is based on per PRB or per PRG basis granularity
  Option 1: per TTI per RBG basis
  Option 2: per TTI per RB basis
  Option 3: per TTI basis
  Make final decisions based above options in next RAN4 meeting
PDSCH demodulation test

## Slide 4
Performance requirements:
  FDD mode:
    Single PMI [2.5], multiple PMI [2.5]
  TDD mode:
    Single PMI: [2.5], multiple PMI [2.5]
Class A PMI test cases

## Slide 5
Test applicability
  Introduce a subset of test cases with different (K, Nmax)
  Based on UE capability, each UE pick up one configuration to pass with following applicability rule to determine {K, Nmax} :
    If UE supporting (K,Nmax) = (8,64), then pass test with (8,64)
    else if UE supporting (K,Nmax) = (4,32) then pass test with (4,32)
    else if UE supporting (K,Nmax) = (2,16) then pass test with (2,16)
    Other wise UE pass test with (2,8)
Test applicability
For Class B K>1 CRI test case
Test number | #1 | #2 | #3 | #4
(K, Ntotal) | (2,8) | (2,16) | (4,32) | (8,64)

## Slide 6
PMI Adaptation
  Fixed PMI through CSR without Beam steering in channel
FRC: 64QAM Rank1
Beam-forming model: Dynamic power scaling method
    Log scale with A = 5 dB, B = -1.3351 dB
    k = 0,1,2,…,K-1
  controls the phase variation, and the phase for m-th sub-frame is denoted by , where is the random start value with the uniform distribution, i.e. , is the step of phase variation, which is defined in Table below, and m is the linear increment of 1 for every sub-frame throughout the simulation .
    =1.2566×10-3 ( 5s Periodicity)
    Test time should be integer multi ples of 5s
Reference Test Point:[70%] with following CRI
Class B K>1 CRI test case

## Slide 7
Performance requirements
  FDD:
    1.1
  TDD
    1.2
Class B K=1 PMI test cases with PMI-config =1

## Slide 8
Test set-up for Channel measurement restriction test
  Transmitted Power in even CSI-RS sub-frames is 9dB lower than other sub-frames (For CSI-RS REs only)
Test set-up for Interference measurement restriction test
  Transmitted Power for TP2 in even CSI-RS sub-frames is 9dB higher than other sub-frames
MR test