## Slide 1: Way Forward on UE RF Requirements for mmWave
Qualcomm Incorporated
3GPP TSG-RAN WG4 Meeting #80 R4-166709
Gothenburg, Sweden, 22-26 August, 2016

## Slide 2: Background
Discussion on the UE RF requirements for NR has started since RAN4#79Bis
Several areas for study were identified:
  Tx Requirements
  Rx Requirements
  Beamforming related requirements
Other areas are FFS

## Slide 3: Background
There is a common view that all the requirements for frequencies above 24GHz will be tested over the air
Definition of the requirements should take into account how these requirements will be tested

## Slide 4: Tx Requirements
Tx Power Related Requirements
  Requirement on EIRP will be introduced
  How the requirement is defined should be studied
  Whether TRP requirement or other alternative requirements are needed or not is FFS
Signal quality requirements
  Signal transmit quality requirements(EVM, frequency accuracy, etc) are needed
  FFS which requirements are needed and how to define them
Emission requirements
  In-band emissions, ACLR, OOBE requirements are needed
  FFS how these requirements should be defined, whether spatial characteristics have to be taken into account or not if yes how
FFS whether other Tx requirements are needed

## Slide 5: Rx Requirements
Sensitivity Requirements
  EIS requirement is needed
  How the requirement will be defined needs to be studied
Blocking Requirements
  ACS, blocking requirements are needed
  FFS how these requirements should be defined, whether spatial characteristics have to be taken into account or not and if yes, how
  For the blocking requirements, realistic values based on actual possible blockers should be considered
FFS whether other Rx requirements are needed

## Slide 6: Beamforming Related Requirements
Whether beam switching delay requirements are needed (the amount of time needed to switch between any two Tx/Rx beams) or not is studied.
  If needed, how the requirement is defined is FFS
Other requirements are FFS