## Slide 1: Way Forward on LAA Multi-node Testing
Huawei, Ericsson, Qualcomm, Nokia
3GPP TSG-RAN WG4 Meeting #80 R4-166971
Gothenburg, Sweden, 22 – 26 August, 2016

## Slide 2: Devices for the tests
For Wi-Fi devices to be used in the test, both APs and STAs, they should be representative and taken off the shelf
For LAA:
  LAA BS supplied by vendors
  LAA UEs should be representative and taken off the shelf
FFS: How to choose Wi-Fi and LAA devices that are used in the tests

## Slide 3: Test Setup
ATT1
Companion victim device
TX/RX
TX/RX
Aggressor device (DUT)
TX/RX
Victim device
Iagg-vic
Ivic-agg
ATT2
ATT3
Companion aggressor device
TX/RX
ATT4
SNRvic
SNRagg
Note: For LAA, both licensed and unlicensed bands should be connected in the test setup
The following test setup is assumed to be a baseline for further discussions

## Slide 4: Device parameter settings
For Wi-Fi devices, both APs and STAs, the default setting is used
For LAA:
  LAA BS: detailed settings are FFS
  LAA UEs: the default setting is used
The parameter settings in the test should be documented for test repeatability
Repeatability of the tests shall be ensured

## Slide 5: Test procedure
To verify co-existence performance between different systems, e.g. LAA to Wi-Fi and Wi-Fi to LAA, each test consists of two steps:
  Baseline test: The performance between the same systems should be tested first and recorded as the baseline.
    Exact baseline performance curve is FFS
  Coexistence test: Replace one Wi-Fi AP with an LAA BS if Wi-Fi is a victim or one LAA BS with a Wi-Fi AP if LAA is a victim and redo the test and record the performance. That means victim Wi-Fi throughput/outage in the scenario of Wi-Fi to Wi-Fi should be the baseline for the scenario of LAA to Wi-Fi; while victim LAA throughput/outage in the scenario of LAA to LAA should be the baseline for the scenario of Wi-Fi to LAA.
Detailed procedure is FFS