## Slide 1: Way forward on co-existence study below 6GHz for NR
CMCC, NTT DoCoMo,KT
R4-167125
3GPP TSG-RAN WG4 #80
Gothenburg, Sweden, 22nd – 26th August 2016

## Slide 2: Background
In RAN4#80, co-existence study for 5G NR below 6GHz was discussed, it is observed that:
  It could be possible to reuse some of the existing co-existence simulation results for LTE and MSR including AAS
  New characteristics for NR, such as new frequency range, new BS and UE antenna and beamforming configuration, may have impact on co-existence results
[1] R4-165064,Consideration on RAN4 NR SI work, NTT DOCOMO INC
[2] R4-166523, On carrier bandwidths for NR in below 6GHz and mm-Wave frequencies, Ericsson
[3] R4-166103, Discussion on co-existence study for frequency below 6GHz, CMCC [4] R4-166203, On below 6 GHz requirement re-use for NR,Ericsson
[5] R4-166202, Co-existence simulation results for NR below 6 GHz, Ericsson
[6] R4-165494, Feasibility of UE UL beamforming for NR, Ericsson

## Slide 3: WF on co-existence study below 6GHz
Beamforming configuraion | Around 700MHz | Around 2GHz | Around 4GHz
No Beamforming | Check the applicability of reusing existing co-existence study results after RAN1 specification becomes clear and stable | Check the applicability of reusing existing co-existence study results after RAN1 specification becomes clear and stable | Check the applicability of reusing existing co-existence study results after RAN1 specification becomes clear and stable
BS Beamforming only | Check the applicability of BS beamforming | Check the applicability of reusing existing co-existence study results such as AAS | Check the applicability of reusing existing co-existence study results such as AAS
BS and UE Beamforming | Check the applicability of UE beamforming | Check the applicability of UE beamforming | Check the applicability of UE beamforming
For a certain case, if the existing co-existence results cannot be reused after applicability checking or no agreement is made, new co-existence study should be conducted
For a certain case,no new co-existence study should be conducted before agreements on the beamforming applicability checking
Note that the frequency ranges selected from TR 38.913 are just examples, the carrier frequency for the co-existence simulation could be further discussed.

## Slide 4: WF on co-existence study below 6GHz
In case the necessity of new co-existence study is identified, make agreement on simulation assumptions
  reuse simulation assumption for existing co-existence study which is suitable for NR as much as possible
  discuss following new parameters
    Carrier frequency for the simulation
    Antenna configuration and beamforming parameters for both BS and UE
    Other parameters are not precluded