## Slide 1: WF on measurement gap enhancement
Intel,
3GPP TSG-RAN WG4 Meeting #81 R4-1609119
Reno, USA, 14 – 18 November 2016

## Slide 2: Per-CC based measurement gap configuration
Per-CC gap offset
  Same gap offset is used for all CC if gap is configured
Measurement gap configuration procedure
Step 1: NW configures the carriers to be measured
Step 2: For each CC, UE indicates all following information to NW
  Need gap or not
    If yes, the gap configuration is indicated
  Need NCSG or not
Step 3: UE indicates updated N_freq to NW.
  This implicates UE’s parallel measurement capability.
  Updated N-frequency cannot be larger than the number of carriers NW configured
Step 4: NW can either honor or override and indicate UE’s per CC gap configuration
  Example 1: if UE indicates 80ms MGRP, NW can override it to 40ms
  Example 2: if UE indicates 40ms MGRP, NW cannot override it to 80ms
  Example 3: if UE indicates no gap, NW can override it to 40ms or 80ms
 | Need Gap | Need interruption control
Indication 1 | Yes and gap configurations | No
Indication 2 | Yes and gap configurations | Yes
Indication 3 | No | No
Indication 4 | No | Yes

## Slide 3: Interruption control for Per-CC gap configuration for synchronous case
In synchronous cases, if UE indicates NCSG is needed for a specific CC (e.g. CC2 in the example below), 1-4-1 NCSG is configured for DL and 1-4-2 SCSG is defined for UL
NCSG should be implicitly configured as shown in Figure below, when measurement gap is configured for some CC(s) but not the other(s). NW does not need to signal UE when NCSG is scheduled.

## Slide 4: Interruption control for Per-CC gap configuration for asynchronous case
In asynchronous cases, if UE indicates SCSG is needed for a specific CC (e.g. CC2 in the example below), 2-4-2 NCSG is configured for DL and 2-4-2 SCSG is defined for UL
NCSG should be implicitly configured as shown in Figure below, when measurement gap is configured for some CC(s) but not the other(s). NW does not need to signal UE when NCSG is scheduled.