## Slide 1: Motivation for New Work Item on Network Based CRS Mitigation
Ericsson
3GPP TSG-RAN WG4 Meeting #81 R4-1610352
Reno, Nevada, USA, 14th - 18th November 2016
Agenda Item: 13

## Slide 2: Background & motivation
LTE transmits CRS across the system bandwidth in every subframe
 High inter-cell interference even at low/medium load
Unnecessarily low per-user throughput, mainly due to higher order modulations not being usable
  High inter-cell interference even at low/medium load
 Inefficient utilization of resources at BS
*) LAA: License Assisted Access

## Slide 3: Network Based CRS Mitigation
Network based CRS mitigation supporting legacy UEs
  A cell omits CRS transmissions if it expects all (connected mode) UEs to be in DRX, but
    maintains CRSs on the inner 6 PRBs continuously (for idle mode support)
  A cell enables CRS when it expects at least one UE to leave DRX
  Aligned on-durations among UEs increase the muting possibilities
Already tested in life networks
  It performs very well with legacy UEs
  No additional RLFs observed
  Up to 80% increased DL throughput in low to medium load (of neighbor cells)
    Especially due to lower utilization of higher order modulation, like DL 256 QAM

## Slide 4: Legacy UE protection
Tested UEs show stable RSRP measurements if CRS in few TTIs before and after DRX on duration is enabled
  The ratio of blanked to non-blanked sub-frames determines feature gain
  Shortening warm-up and cool-down increases performance gains, i.e., per-user throughput
Specify Rel-14 UE perf. requirements for warm-up and cool down phases
  Aim at 1 warm-up and 0 cool-down subframes with full CRS BW
 Higher efficiency of Network based CRS mitigation
Radio frame
Full CRS BW
CRS BW
DRX onDuration
DRX
0
1
2
3
4
Muted CRS
warm-up
cool-down