## Slide 1: WF on channel bandwidth and transmission bandwidth configuration for NR
NTT DOCOMO, INC.,
3GPP TSG-RAN WG4 Meeting #81
Reno, US, 14 - 18 Nov, 2016
R4-1610590

## Slide 2: Background
New concept of definition of channel bandwidth to leverage a wideband spectrum for NR was discussed.
  Channel bandwidth can be determined based on allocated spectrum frequency size and/or BS capability
  Transmission bandwidth configuration for a UE depends on bandwidth the UE supports.
  A UE can camp on the channel regardless of the width of the channel

## Slide 3: WF: Specification impact
Study RF specification impacts as below.
  Identify whether each RF requirement is impacted by the following aspects:
    Transmission BW configuration,
    Channel bandwidth,
    Combination of the two, or
    None (of the aspects)
  Study how each requirement is impacted by the identified aspect (R4-1610170 can be used as reference)

## Slide 4: WF: Implementation impact
Study feasibility of the new concept by comparing following cases from implementation point of view.
  Case 1: UE with single RF chain and BS with single RF chain support wide single channel
  Case 2: UE with single RF chain and BS with multiple RF chains support wide single channel
  Case 3: UE with multiple RF chains and BS with single RF chain support wide single channel
  Case 4: UE with multiple RF chains and BS with multiple RF chains support wide single channel
  Case 1: UE with single RF chain and BS with single RF chain support intra band CA
  Case 2: UE with single RF chain and BS with multiple RF chains support intra band CA
  Case 3: UE with multiple RF chains and BS with single RF chain support intra band CA
  Case 4: UE with multiple RF chains and BS with multiple RF chains support intra band CA

## Slide 5: WF: Implementation impact (2/3)
Channel
BS RF chain
Case 1
Case 2
RF chain X
RF chain A
RF chain B
RF chain X
RF chain A
UE RF chain
Case 3
RF chain X
RF chain Y
RF chain A
Case 4
RF chain X
RF chain Y
RF chain A
RF chain B
Channel
BS RF chain
UE RF chain
Case 5
Case 6
RF chain X
RF chain A
RF chain B
RF chain X
RF chain A
Case 7
RF chain X
RF chain Y
RF chain A
Case 8
RF chain X
RF chain Y
RF chain A
RF chain B

## Slide 6: WF: Implementation impact (3/3)
Identify issues related to implementation for each of case in slide 4
  Both RF part and Digital FE part
  Study the relevance of each of the above cases
  Identify constraints to enable both case 1 and 2 implementation in the same channel
At least following aspects should be studied
  Tx EVM (R4-1609819 can be used as reference)
  Receiver SNDR (signal-to-noise-and-distortion-ratio) performance including Phase Noise (R4-1609659 can be used as reference)
  Different UL/DL bandwidths for UE (R4-1609819 can be used as reference)
  interrelation between supportable Transmission bandwidth configuration and subcarrier spacing (dependent on phase noise etc), supported FFT sizes, RF efficiency considering other RF requirements such as ACLR, sensitivity, blocking etc.
  How a wideband single carrier can be supported from BS viewpoints.