## Slide 1: WF on measurement gap enhancement
Intel, Ericsson, Nokia, Huawei
3GPP TSG-RAN WG4 Meeting #81 R4-1610691
Reno, USA, 14 – 18 November 2016

## Slide 2: Short MGL
RAN4 needs to inform RAN2 that it is decided to specify gaps of length ML= 3 ms. The new gap patterns will be defined as follows
Gap Pattern Id | Measurement Gap Length (MGL, ms) | Measurement Gap Repetition Period (MGRP, ms) | Minimum available time for inter-frequency and inter-RAT measurements during 480ms period (Tinter1, ms) | Measurement Purpose
0 | 6 | 40 | 60 | Inter-Frequency E-UTRAN FDD and TDD, UTRAN FDD, GERAN, LCR TDD, HRPD, CDMA2000 1x
1 | 6 | 80 | 30 | Inter-Frequency E-UTRAN FDD and TDD, UTRAN FDD, GERAN, LCR TDD, HRPD, CDMA2000 1x
2 | 3 | 40 | TBD | Inter-Frequency E-UTRAN FDD and TDD
3 | 3 | 80 | TBD | Inter-Frequency E-UTRAN FDD and TDD

## Slide 3: Window for 3ms gap applicability
When gaps with gap pattern ID 3 or gap pattern ID 4 are configured, the UE shall be able to detect a target cell if the sub frame of the target cell containing PSS/SSS begins not earlier than 500uS from the start of the measurement gap and if the sub frame containing PSS/SSS ends not later than 500uS before the end of the measurement gap. The reference point for this requirement is at the UE antenna connector.

## Slide 4: Per CC Measurement gaps
Background
  Earlier RAN4 provided the following options to RAN2
    Option 1: UE signals capabilities for all supported CA combos when UE attaches to the network
    Option 2: UE signals capabilities on demand (network advertises what it supports and UE replies with related capabilities)
    Option 3: UE signals capabilities based on configured CA combo (UE sends capabilities when configured with a certain CA combo)
    Option 4: UE determines the exact measurement gap configurations per CC and signals NW the corresponding gap pattern ID. NW can override UE’s decision by falling back to legacy per-UE based measurement gap configuration.
    Other options are not precluded
    The discussion on capability signalling option may take place in RAN2

## Slide 5: Aspect of signalling for per-CC measurement Gap
RAN4 has been discussing further information that would be needed for RAN2 to make an informed decision between approaches, and to complete the work for the chosen approach
  Approach A (eg Options 1,2) : Gap capabilities are reported by the UE in advance of configuration of CA and measurements
    eNB may use the information to select a suitable configuration based on its gap needs
    UE does not have the opportunity to optimize its gap configuration once the exact measurement configuration is known.
    Reported gap capabilities can result in a non-optimized indication of need for GAP/NCSG, although UE has sufficient gaps to measure.
  Approach B (eg Option 4) : Gap capabilities are reported by the UE after configuration of CA and measurements
    eNB can configure a measurement gap configuration. Note: eNB does not have the information to optimize gap configuration based on the UEs gap needs
    UE has the opportunity to indicate its optimized gap configuration once the exact measurement configuration is known
    eNB is able to override UE and decide a different gap configuration based on per-UE gap configuration to make sure UE has sufficient gaps to measure.
  Overhead related issue should be discussed and determined in RAN2

## Slide 6: Aspect of parallel measurements with per-CC measurement gap
Background : Since release 8, when multiple measurement objects are configured, the measurement performance has been scaled by a factor Nfreq which corresponds to the number of objects configured
UEs with capable RF and baseband may be capable of performing parallel measurements and perform measurement activities with shorter delay
It would be beneficial for the eNB to be aware that a UE is capable of parallel measurements
This could be achieved by signalling Nfreq,effective <Nfreq
Nfreq,effective depends on
  The CA configuration, which will determine which RF chains are configured
  The per CC gap configuration which will determine which of these RF chains are free in gaps
  The interfrequency measurement object configuration.
  Any UE baseband processing limitation, e.g. UE does not have baseband capability to measure more than X carriers in parallel even if there are multiple RF chains free in gaps
FFS: Nfreq,effective that will be used by the UE is for certain measurement configuration(s) and CA combination(s) is requested by the eNB and provided by the UE assuming a maximal gap configuration

## Slide 7: Approach A
An example of Approach A
  Within the context of the bitmap example in TR36.894, each CA combo is considered to be according to the RAN2 definition of a supportedBandCombination.
  Within the context of the bitmap example in TR36.894, at least the following options are needed for target measurement band for each serving CC: a) No gap needed b) Interrupt control gap needed c) Measurement gap needed
  To simplify the work, a single MGRP/VIRP for all CC configured in each UE can be considered.
  Multiple measurement band configurations can be derived from single measurement band gap configurations using the following rules
    If one or more relevant measurement bands (columns in the table) indicates a need for GAP for a certain CC, the combined result for that CC is GAP.
    If one or more relevant measurement bands (columns in table) indicates a need for INTC for a certain CC (INTC entries are logically “OR’d”) and no other column indicates a need for GAP for that CC, the result is INTC. If any of the columns indicates a need for GAP, rule 1 already indicates that GAP should be configured.
    If all relevant measurement bands (columns in the table) indicate NOGAP for a certain CC, the result is NOGAP (NOGAPS are combined in logical “AND”).
Since the number of combinations of these factors is very high, under option A it would be difficult to signal Nfreq,effective for every possible measurement configuration (ie there are no simple combining rules from which Nfreq,effective for multiple measurement objects can be derived)

## Slide 8: Approach B
Per-CC gap offset
  Same gap offset is used for all CC if gap is configured so that interruptions do not occur with different offsets
Example Measurement gap configuration procedure
Step 1: NW configures measurement/gap according to existing signaling including per UE MGRP
Step 2: For each CC, UE indication to NW includes all following information
  Indication on if gap is needed or not
    If yes, per-CC gap configuration is indicated
    If yes, optionally an indication of a preferred MGRP which may be longer than the per UE MGRP
  Indication on if NCSG is needed or not
    If yes, per-CC gap configuration is indicated
    If yes, optionally an indication of a preferred VGRP which may be longer then the per UE MGRP
  N_freq,effective
    UE’s parallel measurement capability can be indicated by N_freq_effective.
  Note 1: Indication configuration is given in Table 1
  Note 2: The need for indication 2 arises if the UE indicates different MGRP for different CC
 | Need Gap | Need interruption control
Indication 1 | Yes and gap configurations | No
Indication 2 | Yes and gap configurations | Yes and NCSG configuration
Indication 3 | No | No
Indication 4 | No | Yes and NCSG configuration
Table 1: example table of UE indication for per-CC gap configuration

## Slide 9: Approach B (Cont.)
Step 3: NW can either honor or override UE’s indication in step2 and indicate UE’s per CC gap configuration
  Example 1: if UE indicates 80ms MGRP, NW can override it to 40ms
  Example 2: if UE indicates 40ms MGRP, NW can override it to 80ms. In this example, eNB should request UE to provide updated N_freq_effective.
  Example 3: if UE indicates no gap, NW can override it to 40ms or 80ms
  Example 4: If the UE indicates NCSG, the NW can override it to 40ms or 80ms 6ms gap
Step 4: if NW reconfigure measurement object list and gaps according to existing signaling including per UE MGRP, go back to Step 2. Otherwise, the measurement gap configuration is completed

## Slide 10: NCSG
RAN4 needs to inform RAN2 that it is decided to specify NCSG configuration
NCSG Pattern Id | Visible interruption length before measurement (VIL1, ms) | Measurement Length during which there is no gap (ML, ms) | Visible interruption length after measurement (VIL2, ms) | Visible interruption Repetition Period (VIRP, ms) | Purpose
1 | 1 | 4 | 1 | 40 | Interruption control according to requirements in sections x,y,x
2 | 1 | 4 | 1 | 80 | Interruption control according to requirements in sections x,y,x
3 | 2 | 3 | 2 | 40 | Interruption control according to requirements in sections x,y,x
4 | 2 | 3 | 2 | 80 | Interruption control according to requirements in sections x,y,x
It is FFS to introduce other NCSG pattern with VIRP more than 80ms

## Slide 11: Interruption control for Per-CC gap configuration for synchronous case
In synchronous cases, if UE indicates NCSG is needed for a specific CC (e.g. CC2 in the example below), 1-4-1 NCSG is configured for DL and 1-4-2 NCSG is defined for UL
NCSG should be implicitly configured as shown in Figure below. NW does not need to signal UE when NCSG is scheduled.
When NCSG collides with measurement gap, no NCSG is scheduled.

## Slide 12: Interruption control for Per-CC gap configuration for asynchronous case
In asynchronous cases, if UE indicates NCSG is needed for a specific CC (e.g. CC2 in the example below), 2-4-2 NCSG is configured for DL and 2-4-2 NCSG is defined for UL
NCSG should be implicitly configured as shown in Figure below, when measurement gap is configured for some CC(s) but not the other(s). NW does not need to signal UE when NCSG is scheduled.
When NCSG collides with measurement gap, no NCSG is scheduled.
It is noted MGL for SCG is 7ms for asynchronous DC

## Slide 13: Interruption control
  Enable measurement on unused RF chains with interruption controlled on activated CC
    Covered by the information in per CC way forward
  Enable per-CC measurement gap configuration with interruption controlled
    Covered by the information in per CC way forward
  Remove interruptions due to deactivated SCell measurement
    For one or more than one deactivated Scell measurement, UE should provide an per-UE indication if NCSG is needed to control the interruption
      If yes, NCSG or 6ms measurement gap pattern ID should be provided
    Update RAN4 specifications for requirements where autonomous interruptions are currently allowed, and the new interruption control patterns would eliminate interruptions.

## Slide 14: Non-uniform Measurement Gap Pattern
FFS: RAN4 needs to inform RAN2 that it is decided to specify Non-uniform measurement gap pattern configuration:
FFS: A gap burst consist of a number of consecutive gaps repeated with a longer burst repetition period.
  RAN4 will introduce a periodicity of the gap burst.
  RAN4 will define number of gaps per gap burst.
Gap Pattern Id | MeasurementGap Length (MGL, ms) | Measurement Gap Repetition Period (MGRP, ms) | Minimum available time for inter-frequency and inter-RAT measurements during 480ms period (Tinter1, ms) | Measurement Purpose
0 | 6 | 40 | 60 | Inter-Frequency E-UTRAN FDD and TDD, UTRAN FDD, GERAN, LCR TDD, HRPD, CDMA2000 1x
1 | 6 | 80 | 30 | Inter-Frequency E-UTRAN FDD and TDD, UTRAN FDD, GERAN, LCR TDD, HRPD, CDMA2000 1x
2 | 6 | 40 | 60 | Inter-Frequency E-UTRAN FDD and TDD, UTRAN FDD, GERAN, LCR TDD, HRPD, CDMA2000 1x