## Slide 1: WF on baseline and reference receiver for BS IC
Nokia, China Telecom, ZTE, Huawei, [Samsung]
3GPP TSG-RAN WG4 Meeting #81
Reno, Nevada, USA, 14 - 18 November, 2016
R4-1610712

## Slide 2: Background: agreements in RAN4 #80bis
Reference Receiver
  Option 1: CWIC
    CWIC is used to mitigate uplink intra-cell inter-user interference
    IC iteration may or may not be implemented to further improve the receiver performance
    the Rel-13 BS MMSE-IRC receiver can be applied simultaneously for inter-cell interference suppression while CWIC receiver is used for intra-cell interference cancellation, if inter-cell interference are to be modelled
  Option 2: SLIC
  Down-selection to be made in the next meeting by taking complexity and performance into consideration
Baseline receiver for performance comparison
  MMSE receiver for intra-cell interference scenario only
  Rel-13 BS MMSE-IRC for inter-cell interference suppression, if inter-cell interference are to be modelled
Open issues for intra-cell UEs:
  Number and Spatial correlation level for the multiple co-scheduled UEs within the target cell for BSs with different Rx antennas
    The definition and modeling of different correlation levels need to be discussed
  Number of intra-cell interferers / layers to be cancelled for BSs with different Rx antennas

## Slide 3: WF on baseline and reference receiver
Use MMSE-IRC receiver as the baseline receiver
In multi-cell scenario, for both baseline and reference receivers, implement inter-cell interference and noise whitening, i.e., inter-cell interference suppression with MMSE-IRC
  Note: following the definition in TR 36.884, DM-RS symbols are used to estimate the inter-cell interference covariance matrix, and the estimation of interference covariance matrix is performed at per PRB and per TTI basis.
CW-IC receiver is used for intra-cell inter-user interference mitigation in the reference receiver.

## Slide 4
  For 2Rx BS: 2 intra-cell UEs
  For 4/8Rx BS:
  Option 1: 4 intra-cell UEs [implement at most 2 or 3 rounds of decoding]
  Option 2: 4 intra-cell UEs and 2 UEs per spatial layer
    [for UEs within the same spatial layer, implement CW-IC]
    [for UEs in different spatial layers, implement IRC to suppress the inter-user interference]
  Option 3: 2 intra-cell UEs
  Keep three options open and make down-selection in the next meeting
  Note: the text in [] is for companies’ reference for simulator setup and result alignment, and it is FFS whether to capture these text into the TR
WF on handling of intra-cell UEs