## Slide 1: WF on NR spectrum utilization
Huawei, HiSilicon, […]
3GPP TSG RAN WG4 Meeting #81 | R4-1610922
Reno, USA, 14 – 18 Nov 2016 | 

## Slide 2: Background(1/2)
As agreed in RAN4#80bis,
  Carrier spectrum utilization, denoted by Y, is assumed to be higher than 90% in RAN4 future study and RAN4 requirements should be defined based on this assumption.
    Y may depend on specific numerology and carrier bandwidth. It is FFS how the guard band at the edge of a channel should be defined when different numerologies are frequency multiplied
    Y may depend on the BS/UE implementation complexity and declared capability. It is possible to define different value of Y for different BS/UE capabilities
Companies’ preliminary evaluation results show that,
  The max. Y varies with numerology, carrier bandwidth and spectrum confinement techniques.
  For some combinations of bandwidth and subcarrier spacing e.g. 10MHz@120kHz and 5MHz@60kHz, Y is below 90% [R4-1609662(ZTE)].

## Slide 3: WF
For some combinations of bandwidth and subcarrier spacing e.g. 10MHz@120kHz and 5MHz@60kHz, the theoretic maximum spectrum utilization Y will be below 90% when integer number of PRBs are used for the transmission bandwidth configuration as in LTE.
  How to improve Y over 90% is FFS.
The maximum spectrum utilization based on RAN4 requirements may vary with numerology, carrier bandwidth and different BS/UE capabilities, considering the capabilities of spectrum confinement techniques including both filtering and windowing , e.g., indicated as a range [YL, YH] for each group of (BW subset @ SCS subset) .
  How to group (BW subset @ SCS subset) is FFS.
  YL and YH are with compliance of related RF requirements, e.g. EVM, ACLR, SEM, selectivity, demodulation etc.
    EVM evaluation should include high order modulations up to 256QAM.
  FFS for UE capability needed or not
The guard band for a carrier in case of mixed numerology may be asymmetric and defined with the assumption that only single numerology is applied, and the assumed numerology refers to the numerology applied at band edge.
The need and size of GB between two numerologies is FFS. The granularity of GB, i.e. 1 PRB or fractional PRB, will be further evaluated.

## Slide 4: Aspects to Analyze (1/3)
Compare filtering and windowing,
  To decide the guard band at the edge of the channel the analysis should focus on the following aspects:
    Emission levels complying with SEM while achieving highest spectrum utilization
    EVM analysis over the entire channel bandwidth (preferably per RB)
    Impact of uneven EVM
    Impact of spectrum confinement techniques to ISI (i.e. BLER performance in fading channel)
    Complexity of spectrum confinement technique used (complexity of the filter used)
    Impact of PA over emission levels and EVM (Start with the PA models and operating points used in RAN1 evaluation. PA models with memory effects are not ruled out)
    Impact to ICI is FFS
    Impact to other timing critical procedures
    Coexistence to LTE in applicable bands

## Slide 5: Aspects to Analyze (2/3)
Compare filtering and windowing,
  To decide the guard band between different numerologies within the same channel the analysis should focus on the following aspects:
    Required in-band emissions levels (emissions from one numerology into the other)
    EVM in the subband assigned to each numerology
    Impact of uneven EVM
    Impact of spectrum confinement techniques to ISI (i.e. BLER performance in fading channel)
    Assumptions on the filter used for the EVM measurement (complexity of the filter)
    Impact of PA over emission levels and EVM (Start with the PA models and operating points used in RAN1 evaluation. PA models with memory effects are not ruled out)
    Impacts to other timing critical procedures
Companies should provide the details of the simulation configuration and the parameters of any spectrum confinement techniques applied.

## Slide 6: Aspects to Analyze (3/3)
For some combinations of bandwidth and subcarrier spacing e.g. 10MHz@120kHz and 5MHz@60kHz, the theoretic maximum spectrum utilization Y will be below 90% when integer number of PRBs are used for the transmission bandwidth configuration as in LTE.
  How to improve Y over 90% is FFS.
For spectrum utilization in cases where utilization is <90% with integer number of PRBs
  Actual use cases for these combinations of CHBW and SCS
  Number of bits that can be transmitted in 1 TTI with integer and fractional number of PRBs

## Slide 7: Reference
Spectrum utilization
  [1] R4-1609945, Ericsson
  [2] R4-1609647, Qualcomm
[3] R4-1609662, ZTE
[4] R4-1609357, Samsung
[5] R4-1609411, Huawei
[6] R4-1609412, Huawei
In-band requirements for mixed numerology
[1] R4-1609221, Nokia
[2] R4-1609223, Nokia
[3] R4- 1609225, Nokia
[4] R4- 1609227, Nokia
[5] R4- 1609219, Nokia
[6] R4- 1609413, Huawei
[7] R4- 1609414, Huawei