## Slide 1: Way Forward on 2TX for RRM
Ericsson, Nokia
R4-1702138

## Slide 2: Background
It is desirable in the feMTC WI to improve mobility performance
  Mobility is based on RSRP estimates and derivatives therefrom
It is further desirable in the feMTC WI to improve PRACH repetition level selection performance
  PRACH repetition selection is based on RSRP estimates
Legacy UE categories estimate RSRP using 2 RX branches and 1 TX port (2 TX ports are allowed)
New UE categories estimate RSRP using 1 RX branch and 1 TX port (2 TX ports are allowed)
In practice 2 TX ports are needed for supporting demodulation performance requirements in CE mode B
Simulation results provided to RAN4#82 indicate that the increased diversity when measuring using 1 RX over 2 TX may improve the RSRP accuracy and thus the mobility performance

## Slide 3: Agreements
The RSRP measurement performance for 1RX/1TX and 1RX/2TX shall be investigated for measurement bandwidths 6, 24 and 96 PRBs
A suitable applicability rule for RSRP measurements on 2TX ports shall be investigated, for mobility and PRACH level selection, respectively
Interested companies are invited to provide to the RAN4#82bis meeting in Spokane:
RSRP measurement performance for 1RX/1TX and 1RX/2TX
  RS-SNR range -20 to 10 dB
  Propagation conditions: AWGN, ETU1, EPA1, ETU30, EPA5
Applicability rule for measurements on 2TX ports
Combining schemes for TX port 0 and TX port 1 (average, max, ...)