## Slide 1: WF on Hybrid requirements
NEC, Huawei
3GPP TSG-RAN WG4 Meeting #82 R4-1702263
Athens, Greece, 13-17 Nov, 2017

## Slide 2: Background
WF in [1] Agreed as:
    When the full OTA AAS requirements are introduced there for AAS BS which retain a conducted interface there will be a set of hybrid requirements (mixture of conducted and radiated requirements) which they can choose to apply . The format of the hybrid requirements is still under discussion. The following hybrid specifications have been identified and discussed
    1. Use the existing REL13 requirements (i.e. full set of conducted requirements with 2 OTA requirements).
    2. Have a new set of requirements with some of the conducted requirements as OTA requirements.
    3. Have 2 or more hybrid options (including options 1 and 2).
    4. Have a set of requirements where certain requirements may be either conducted or OTA not both.
    Contributions further investigating the pro’s and con’s of each option as well as opinions of which solution is suitable are encouraged.
During this meeting a number of contributions submitted with proposal on the Hybrid requirements in [2] [3] and [4].

## Slide 3: Agreement
It is agreed to include in AAS Rel-14 specifications a set of OTA Requirements as per the current Scope of the WID and additional set of One or more Hybrid requirements.
The OTA requirements set shall apply to OTA AAS BS which does not have conducted interface (i.e. access to connectors are not available for conducted testing).
A hybrid AAS BS, i.e. An AAS BS with conducted interface and OTA interface (i.e. access to connectors available for conducted testing), either the OTA requirements set or any (if more then one is specified) of the hybrid requirements set(s) can be applied.
All the requirements (conducted and the two OTA requirements) in AAS Rel 13 specifications (TS 37.105 -1 and -2) are considered as one of the Hybrid requirements sets.
Additional hybrid requirements set(s) either fixed, e.g. Rel-13 AAS requirements as indicated above, or flexible set in which mapping of requirements to either conducted or OTA domains are not fixed but rather declared by vendors will be further investigated with open issues as identified in the following slide.

## Slide 4: Open Issues to be address for setting additional Hybrid requirements set
To consider fixed list and/or flexible additional Hybrid requirements set with mapping of requirements in either the conducted domain or the OTA domain but not both.
  Example of a fixed Hybrid requirement is a set which include all conducted and radiated requirements as is currently specified in Rel-13 AAS specifications.
  A flexible Hybrid requirement will include a minimum sub-set of OTA requirements (FFS) and vendors can then define their own remaining requirements in either the conducted or radiated domains.
For some requirements, either OTA or conducted, have dependency on other requirements. As an example, the OTA blocking requirements depends on OTA sensitivity.
  In such case if a requirement is selected to be included in a domain, e.g. either OTA or Conducted, all dependent requirements for that requirements shall be maintained in its corresponding requirement domain.

## Slide 5: References
R4-1610805, WF on the hybrid requirements, Huawei.
R4-1701057, On the topic hybrid requirements, Ericsson
R4-1701694, Proposal on Hybrid Requirements for eAAS, NEC
R4-1701721, Hybrid requirements analysis, Huawei