## Slide 1: 3GPP TSG-RAN WG4 Meeting #82Bis Spokane, Washington, USA, 03 – 07 April, 2017
Huawei
Way forward on eLAA BS demodulation performance
R4-1703748

## Slide 2: Background
As per the agreed WF R4-1702146 in RAN4#82 Athens meeting, many agreements were reached, but still some open issues were left for eLAA BS demodulation performance requirements.

## Slide 3: General
Test Purpose:
  Verify PUSCH new interlace resource structure
  Verify PUSCH demodulation performance with UL LBT model
Ending symbol configuration
  Up to SC-FDMA symbol 12
Resource allocation
  Contiguous interlace allocation
    One or more interlace allocation is TBD
Channel model
  EPA5 Low
Modulation
  QPSK 1/3 and 16QAM ¾

## Slide 4: UL burst transmission model
UL burst transmission model needs to be defined as following:
  One burst is defined as uplink transmissions which occupy one or more consecutive subframes. The burst transmission format is determined as described below:
  Select the number of subframes randomly from a given set of the number of subframes {1, 2, 3, 4} with equal probability as the total length of one burst transmission. The length includes both occupied SC-FDMA symbols and non-occupied SC-FDMA symbols within the burst format. The starting position of the first scheduling subframe is 25us in symbol 0. The PUSCH ending symbol is second to last symbol of the last subframe.
  A uniform random variable from [0, 1] is generated. If the random variable is less than p= 0.5
    If both the last subframe of previous burst and first subframe of new burst format are fully occupied, start burst transmission after deferring one subframe from the last subframe of previous burst. Otherwise, start burst transmission at the end of last subframe of previous burst.
  Otherwise, the burst transmission is muted and the muting duration is the same as the number of subframes for determined burst format.
Companies are welcome to provide simulation with UL burst transmission model for RAN4#83 meeting.