## Slide 1: WF on Channel bandwidth related terminology
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 #82bis Meeting Spokane, WA, USA, 3 - 7 April, 2017
R4-1704224

## Slide 2: Background
It was agreed in RAN1 to introduce a new methodology that a NR UE can access to a NR cell regardless of system bandwidth in the cell.
In RAN4, it was proposed for NR to define the following terminologies. [1]
  Channel bandwidth (CBW): RF bandwidth supporting single carrier in a cell provided by gNB -> namely, system BW
  UE Maximum Bandwidth (UMBW): Maximum bandwidth which a NR UE can transmit and/or receive.
    Note: UMBW is a UE specific and can be different between Tx and Rx
Further clarification was required in the online session.

## Slide 3: WF on CBW
  Channel bandwidth (CBW): Operating contiguous BW supported by gNB (1CC) in which UE is operated -> namely, system BW
  Limited number of CBW should be specified in Rel-15.
  CBWs are dependent on operating band, etc
  CBW is declared by BS manufactures, which is the same as LTE cases
  New CBWs (smaller(middle) or larger) can be added in later releases and Rel-15 UE can be operated in New CBWs.
    The emission requirements of UE are based on “CBW” like Cat.Mx UE mask.
    To specify the emission requirements such as SEM so that values of smaller CBW is tighter than those of larger CBW. With this, even if 150 and 300 MHz CBW are introduced in a later release, the UE can obviously satisfy the SEM without testing by meeting that of 100 and 200 MHz CBW.

## Slide 4: WF on UMBW
UE Maximum Bandwidth (UMBW): Maximum contiguous bandwidth which a NR UE can transmit and/or receive.
  UMBW is a contiguous BW within a band.
  UMBW can vary with respect to each operating band, SCS, number of contiguous CCs etc.
  UMBWs are not specified in the RAN4 spec and depend on the UE Capability.
  UMBWs are signaled from UE to gNB with indication of non-CA or CA.
    for example, if UMBW is 400MHz UE can signal that it supports this as 2x200MHz even if 400MHz is supported as a single carrier
  The UE needs to satisfy the requirements for each CBW not exceeding the UMBW.
  UMBW can be larger than CBW.
  UMBW is a UE specific and can be different between Tx and Rx
  Granularity of CBW and UMBW is FFS.
  Non-contiguous cases shall also be available, how to treat it is FFS.

## Slide 5: Reference
[1] R4-1703563 Consideration on flexibility of NR Channel Bandwidth Source: NTT DOCOMO, INC.