## Slide 1: WF on Enhanced CRS-IM Performance Requirements
Intel Corporation, LGE, CATT
3GPP TSG-RAN WG4 Meeting #82bis Spokane, USA, 3 - 7 April 2017
Agenda Item: 7.27
R4-1704230

## Slide 2: Introduction
CRS-IM enhancements work objectives:
  Stage 1: Investigate performance benefits and feasibility of using CRS-IM receivers:
  Stage 2: Specify UE demodulation and CSI reporting performance requirements to verify practical CRS-IM operation for the identified scenarios based on the outcome of Stage 1.
RAN4 #82 agreements
  R4-1702195 WF on Enhanced CRS-IM Performance Requirements
  R4-1702451 WF on simulation assumptions for Enhanced CRS-IM initial studies
This WF provides further agreements on the target scenarios and reference receivers for the Stage 1 investigations of CRS-IM enhancements and downselection of test cases and parameters for Stage 2 work
Companies are encouraged to provide further inputs on the scenarios and reference receivers performance/complexity analysis in RAN4 #83

## Slide 3: Enhanced CRS-IM for PDSCH (1)
Background: Candidate scenarios in RAN4 #82
Further refinement of test parameters for Test cases 1, 2, 3, 4
  Use MCS 21 for Test 4
Test | TM | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  |  | Serv. cell | Interf. cell
Test cases for performance requirements definition |  |  |  |  | 
1 | TM4 | Non Colliding | 2 | 4 | 4
2 | TM4 | Non Colliding | 4 | 2 | 2
3 | TM9 | Non Colliding | 4 | 2 | 2
4 | TM4 | Non Colliding | 4 | 4 | 4
Test cases for additional analysis / discussion |  |  |  |  | 
5 | TM4 | Colliding | 2 | 4 | 4
6 | TM4 | Colliding | 2 | 4 | 2

## Slide 4: Enhanced CRS-IM for PDSCH (2)
Test case 5
  Confirm performance gains of CRS-IM Receiver #2 (R4-1702195) based on summary of alignment results.
    TR should also mention blind detection feasibility notes
  Do not define performance requirements
Test case 6
  Confirm performance gains of CRS-IM Receiver #1 and #2 (R4-1702195) based on summary of alignment results. .
  Do not define performance requirements

## Slide 5: Enhanced CRS-IM for PDCCH/PCFICH (1)
Background:
  Candidate scenarios
  RAN4 #82 agreements
    Confirm CRS-IM feasibility and define requirements for TC 1.
    Deprioritize work for TC2
    Continue studies for additional PDCCH/PCFICH TC3 (investigate both performance and complexity).
Test | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  | Serv. cell | Interf. cell
1 | Non Colliding | 2 | 4 | 4
2 | Non Colliding | 4 | 2 | 2
3 | Non Colliding | 4 | 4 | 4

## Slide 6: Enhanced CRS-IM for PDCCH/PCFICH (3)
Test 3 (4 RX antennas + 4 CRS APs)
  Provide additional analysis in RAN4 #83 for Medium correlation channel model
  Decide on performance requirements introduction in RAN4 #83
    Option 1: Do not define requirements
    Option 2: Define demodulation requirements for Medium antenna correlation model based on Type A CCIM receiver
    Option 3: Define demodulation requirements for Medium antenna correlation model based on LMMSE-IRC receiver
    Option 4: Define demodulation requirements for Low antenna correlation model based on LMMSE-IRC receiver (without CRS-IM)

## Slide 7: Enhanced CRS-IM for PHICH (1)
Background:
  Candidate scenarios
  RAN4 #82 agreements
    Confirm performance gains for PHICH TC 1. FFS if performance requirements need to be introduced.
    Deprioritize work for TC2
    Continue studies for additional PHICH TC3 (investigate both performance and complexity).
Way forward: Do not introduce PHICH performance requirements
Test | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  | Serv. cell | Interf. cell
1 | Non Colliding | 2 | 4 | 4
2 | Non Colliding | 4 | 2 | 2
3 | Non Colliding | 4 | 4 | 4

## Slide 8: UE Feature List
Ad-hoc agreements
  Set of UE features
    #1: Non-colliding CRS-IM receiver for 2RX and 4 CRS APs for PDSCH
    #2: Non-colliding CRS-IM receiver for 4RX and 2 CRS APs for PDSCH
    #3: Non-colliding CRS-IM receiver for 4RX and 4 CRS APs for PDSCH
    #4: Type A CCIM receiver for 2RX and 4 CRS APs for DL Control Channels
FFS depending on the test case introduction
  #5: Type A CCIM receiver for 4RX and 2 CRS APs for DL Control Channels
  #6: Type A CCIM receiver for 4RX and 4 CRS APs for DL Control Channels
FFS depending on the capability signalling discussion
  #7: Blind detection of base CRS assistance information including number of CRS-APs