## Slide 1: WF on GNSS side conditions for V2V performance requirements
Intel Corporation, Qualcomm, CATT, LGE
3GPP TSG-RAN WG4 Meeting #82bis Spokane, USA, 3 - 7 April 2017
Agenda Item: 7.15.3
R4-1704280

## Slide 2: Background
Two types of GNSS side conditions for RRM performance requirements were defined in TS 36.133 for the scenarios when GNSS assistance is available and for the conditions when it is not available
  GNSS Condition #1: The conditions for GNSS reliability requirements are defined in Table 6.7 in TS 36.171 when GNSS assistance data available at the UE.
  GNSS Condition #2: The conditions for GNSS reliability requirements are defined in Table B.6.1-1 when there is no GNSS assistance data available at the UE.
  GNSS side conditions for V2V/V2X RRM performance requirements are ambiguous and conformance test case cannot be defined
  For V2V/V2X UE demodulation performance requirements similar GNSS side conditions are expected to be used
  RAN4 does not have consensus on the possible impacts of GNSS assistance availability on the test duration
    Some companies think that in case GNSS assistance is not available the test duration may be large (e.g. > 15min)

## Slide 3: Way Forward
GNSS side conditions and availability of GNSS assistance information are FFS and need to be decided for the RRM performance requirements definition
  Option 1: Use GNSS Condition #1
  Option 2: Use GNSS Condition #2
  Option 3: Use GNSS Condition #1 and GNSS Condition #2
  Option 4: Do not define the performance requirements
Request RAN5 on further inputs on the feasibility of using GNSS side Condition #1 and #2
  e.g. impact on test time, feasibility of providing GNSS assistance
Companies are encouraged to provide more details on the expected inputs from RAN5 and draft LS in RAN4 #83