## Slide 1: Way forward on eFD-MIMO performance requirements
Samsung, Qualcomm, Intel, Huawei, [CATT]
3GPP TSG-RAN WG4 Meeting #82bis Spokane, US, 3 - 7 April, 2017
R4-1704302

## Slide 2
No BS performance requirements needed for Rel-14 eFD-MIMO WI
At least below UE performance test cases needed for Rel-14 eFD-MIMO WI
  New Class A PMI test cases
  New PDSCH demodulation test cases for semi-open MIMO transmission
  New PMI/RPI test case for advanced CSI codebook
  New CSI test case(s)for Hybrid CSI reporting mechanism
  PDSCH demodulation test case for AP ZP-CSI-RS transmission
  CSI test cases for Multi-shot CSI-RS and Aperiodic NZP CSI-RS
UE performance test cases will be introduced under 2Rx
UE performance test cases will be introduced under TM9 mode
Work scope

## Slide 3
Introducing new Class A PMI test cases in Rel-14 eFD-MIMO WI
  Introduce two Class A PMI test cases in Rel-14 eFD-MIMO with different antenna ports:
    One test case for wideband PMI reporting
      FFS on details test setup
    One test case for sub-band PMI reporting
      FFS on details test setup
  At least 32 ports should be covered in one of the test cases.
The demodulation test case(s) will be introduced for semi-open-loop transmission.
RAN4 will introduce new PMI/RPI reporting tests for the advanced CSI codebook
UE performance test cases will be introduced under 2Rx
UE performance test cases will be introduced under TM9 mode
FFS for introducing BS performance requirements for uplink DMRS enhance cement
Agreements

## Slide 4
Introduce two Class A PMI test cases in Rel-14 eFD-MIMO with different antenna ports:
  One test case for wideband PMI reporting
    Option 1: 28 port with CDM4
    Option 2: 24 port with CDM4
  One test case for sub-band PMI reporting
    32 port with CDM8
CSI-RS reduced density for non-precoded CSI-RS resources will be covered by Class A wideband PMI test case
  FFS test applicability
Pending on UE capability, random selection CSS configuration from UE supported list; and defining minimum performance requirements applicable for all CSS configurations.
Reusing test metric as Rel-13 Class A PMI test case as baseline
Class A PMI test cases

## Slide 5: MIMO correlation Matrix for Class A codebook
Reusing existing values for parameters α1, α2, β and γ for high spatial correlation as baseline, Further confirmed by companies’ simulation results
High spatial correlation |  |  | 
a1 | a2 | b | g
0.9 | 0.9 | 0.9 | 0.3
Note 1: Value of α1 applies when more than one pair of cross-polarized antenna elements in first dimension at eNB side. Note 2: Value of α2 applies when more than one pair of cross-polarized antenna elements in second dimension at eNB side. Note 3: Value of β applies when more than one pair of cross-polarized antenna elements at UE side. |  |  | 

## Slide 6
Test metric: existing test metric for PMI test case as relative throughput ratio under FRC as starting point: FFS for detailed random PMI approach
  Option1: randomize only {i1,3, i2, RPI}
  Option2: randomize {i1,1, i1,2,i1,3, i2, RPI}
  Other options not excluded
Introducing test case under rank2 transmission
Beam steering modelling:
  Option 1: introducing at least two cluster Beam direction with separate channel matrix
  Other options not precluded
PMI/RPI reporting test for the advanced CSI codebook

## Slide 7: PDSCH demodulation test cases for semi-open MIMO transmission
Introduce both Rank1 and rank2 test cases
FFS for :Beam-forming modeling
  Option 1: Using Random Beam-forming model
  Other options not excluded
Fading channel: EVA70Hz

## Slide 8: PDSCH performance test case for AP ZP-CSI-RS transmission
Based on Replacing one of existing test cases with Periodic ZP CSI-RS
  Replacing Periodic ZP CSI-RS as AP ZP CSI-RS
  Sub-frames for AP ZP-CSI-RS same as Periodic ZP CSI-RS SFs, the indicated AP ZP-CSI-RS configuration is random selected from RRC-configured AP ZP CSI-RS list
FFS for which existing test case can be used
FFS for applicability

## Slide 9: Simulation assumption for Class A PMI (Information Only)
Parameter | Unit | Test 1(Single PMI test) -28/24 ports | Test 2 (Multiple PMI test) -32 ports
Bandwidth | MHz | 10 | 10
Transmission mode |  | 9 | 9
Propagation channel |  | EPA5 | EVA5
Precoding granularity (only for reporting and following PMI) |  | 50 | 6
Correlation and antenna configuration |  | 2D High XP Option 1: 28 *2 Option 2: 24*2 | 2D High XP 32 x 2
Beamforming model |  | [Annex B.4.3] | [Annex B.4.3]
Cell-specific reference signals |  | Antenna ports 0,1 | Antenna ports 0,1
CSI reference signals |  | Antenna ports | Antenna ports
 |  | FFS | 15,…,46
Number of CSI-RS ports |  | Option 1: 28 Option 2: 24 | 32
CDM Type |  | CDM4 | CDM8
CSI-RS periodicity and subframe offset TCSI-RS / ICSI-RS |  | 5/1 | 5/1
NZP-CSI-RS-Configuration-List |  | FFS | {0,1,2,3}
FrequencyDensityNonPrecoded |  | FFS | 1
NZP-TransmissionCombNonprecoded |  | FFS | NA
eMIMO-Type |  | Class A | Class A
codebookConfig-N1 |  | FFS | FFS
codebookConfig-N2 |  | FFS | FFS
codebook-Over-Sampling-RateConfig-O1 |  | 8 | 8
codebook-Over-Sampling-RateConfig-O2 |  | 4 | 4
Codebook-Config |  | 1,2,3,4 | 1,2,3,4
codebookSubsetRestriction-1 |  | FFS | FFS
codebookSubsetRestriction-2 |  | FFS | FFS
Reporting mode |  | PUSCH 3-1 | PUSCH 1-2
Reporting interval | ms | 5 | 5
PMI delay | ms | 8 | 8
Measurement channel |  | FFS | FFS
Rank Number of PDSCH |  | FFS | FFS
Max number of HARQ transmissions |  | 4 | 4
Redundancy version coding sequence |  | {0,1,2,3} | {0,1,2,3}