## Slide 1: WF on RX spurious requirements
NTT DOCOMO, INC.,
R4-1704328
3GPP TSG-RAN WG4 Meeting #82
Spokane, US, 3rd – 7th April, 2017
Agenda Item: 9.12.2.6

## Slide 2: Background
Receiver spurious emission requirements are discussed in [1-2] in RAN4#82bis meeting.
This contribution summarizes agreement and way forward on this topic.
[1] R4-1703451, “Receiver spurious emissions requirements for eAAS” NTT DOCOMO, INC.
[2] R4-1703945, “Rx spurious requirement OTA” Huawei

## Slide 3: Agreements
For Rel-15 eAAS for FDD
  For both core/conformance specification, OTA receiver spurious emissions requirement will not be applied and be superseded by the TX spurious requirements, since TX and RX spurious emissions cannot be distinguished in OTA region.
For Rel-15 eAAS for TDD
  For core specification, OTA receiver spurious emissions requirement should be applied during the transmitter OFF period only.
  For conformance specification, applicability is FFS.

## Slide 4: Way forward
OTA testability of RX spurious emission for TDD during TX OFF period should be provided in RAN4#83 meeting.
  For the evaluation, it is assumed that the required emission level will be base on the conducted one (Loss factor will be depend on another discussion).