## Slide 1: WF on Maximum Channel Bandwidth
Qualcomm Incorporated
3GPP TSG-RAN WG4#82 Bis
Spokane, USA, April 3rd-4th, 2017
R4-1704350
Agenda : 10.3.1
Document for: Approval

## Slide 2: Support of New Channel Bandwidths
Addition of a new channel bandwidths should be allowed in a future release
  Handling of a CHBW with CA by the UE needs to be supported in the specifications for forward compatibility
  gNBs will have to handle UEs that support CHBW with CA such that legacy UEs can still use entire UMBW
CHBW 400MHz
CHBW 400MHz
UMBW 800MHz
400MHz
400MHz
UMBW 800MHz
400MHz
400MHz
CHBW 800MHz
Rel.15
Rel.16
Addition of
800MHz CHBW
gNB
UE

## Slide 3: Agreements
Addition of new channel bandwdiths is allowed in future releases
  RAN1 design should ensure forward compatibility, send LS to RAN1 to inform about this agreement
UE is allowed to support CHBW with CA combinations
  For example, with 400MHz CHBW UE can support 2x200MHz or 4x100MHz
    UE can process the “CCs” independently from a baseband point of view
  Which combinations are allowed is FFS

## Slide 4: Maximum channel bandwidth (CHBW) in Rel. 15
For bands below 6GHz
  100MHz maximum CHBW
For bands above 24GHz
  200MHz maximum CHBW
Larger channel bandwidths can be introduced in future releases