## Slide 1: WF on Subcarrier Spacing for NR
Qualcomm Incorporated
3GPP TSG-RAN WG4#82 Bis
Spokane, USA, April 3rd-4th, 2017
R4-1704400
Document for: Approval

## Slide 2: Agreements on SCS
SCS supported for bands in below 1 GHz
  15kHz, 30kHz
  60kHz will not be supported pending RAN1 check
SCS supported for bands between 1GHz and 6GHz
  15kHz, 30kHz, 60kHz
SCS supported for bands above 24GHz and below 52.6GHz
  60 kHz, 120kHz for data and control
  240kHz for control and sync
    240 for data can be further considered if a clear benefit is shown