## Slide 1: WF on Multi-node tests for Rel-13 LAA
Qualcomm, Ericsson, Huawei, HiSilicon, Nokia, Alcatel-Lucent Shanghai Bell, US Cellular, Skyworks, AT&T, T-Mobile USA, Verizon, Vodafone, Deutsche Telekom, Broadcom
3GPP TSG-RAN WG4 #82bis
April 3rd – 7th, 2017
Spokane, Washington, USA
R4- 1704409

## Slide 2: Background information: Study item scope
Multi-node study item scope
  This study item is to investigate how to conduct multi-node tests involving two Rel-13 LAA BSs or one Rel-13 LAA BS and one other wireless system, e.g. Wi-Fi system to make sure that the two systems can coexist in the same unlicensed spectrum. In particular, the following goals shall be met by the multi-node testing:
    The tests shall be designed in a way that cross technology coexistence can be achieved. More specifically, the impact for both LAA to other systems, e.g. Wi-Fi and other systems e.g. Wi-Fi to LAA should be tested.
    The testing complexity should be kept as low as possible so it can be easily performed by the operators who have different systems deployed in the same area.
    The tests shall be easily extended to include future systems such as eLAA in Rel-14.
  The outcome of this SI is a TR that will capture the agreed multi-node tests for Rel-13 LAA.

## Slide 3: Purpose and goal of TR 36.789
Based on the Multi-node study, the outcome of Multi-node test SI should be an evaluation methodology which allows to assess the impact for both LAA to other systems, e.g. Wi-Fi and other systems e.g. Wi-Fi to LAA
The evaluation methodology needs to provide the necessary tools to run the coexistence tests, including:
  Test setup, e.g. number of nodes
  Signal levels and SIR operating points
  Evaluation metrics
  …
The scope of TR 36.789 is not to mandate a specific implementation

## Slide 4: Work Plan
RAN4 #82bis: approve a Way Forward addressing all the open issues
RAN4 #83: finalize the TR by implementing the Way Forward agreed in RAN #82bis

## Slide 5: Background info: test setup

## Slide 6: Receiver signal levels and SIR
Two possible methodology:
  Methodology A: two test levels, with received interference signal level above and below ED (Link A-B)
    Above ED configuration:
      AP-STA: -57dBm, AP-eNB: -67dBm, eNB-STA: -67dBm. => SIR: 10dB
    Below ED configuration
      AP-STA: -70dBm, AP-eNB: -80dBm, eNB-STA: -80dBm => SIR: 10dB
    Same levels should be applied when Wi-Fi is aggressor and LAA is Victim
THIS SLIDE IS FFS

## Slide 7: Traffic Types
The following scenarios are considered
Tests with voice traffic on the aggressor link will be made only if the LAA eNB supports voice. If it doesn’t support voice, test 3 won’t be performed and tests 2 and 4 will have only Best Effort in the aggressor link
Scenario 2 and 4 are FFS
Throughput tests |  | 
Scenario | Traffic in victim link | Traffic in aggressor link
1 | Best effort | Best effort
[2 | Best effort | Best effort + Voice]
Outage tests |  | 
Scenario | Traffic in victim link | Traffic in aggressor link
3 | Voice | Voice
[4 | Voice | Best effort + Voice]

## Slide 8: Evaluation metrics
Performance metrics
  Throughput tests: throughput or normalized throughput
  Outage tests: FFS (options: MOS score and/or Jitter and/or outage)
The evaluation process should assess the following percentile points of the performance distribution
  Option 1: 50%
  Option 2: 25%, 50%
  Option 3: 50%, 75%
  Option 4: 25%, 50%, 75%
  Which option to use is FFS

## Slide 9: Other agreements
All 802.11 devices in the tests shall be configured to use the same maximum COT as LAA devices.
The test shall document all pertinent configuration parameters used in the test which relate to the COT. This includes especially, but is not limited to, configuration parameters that may be set differently in the tests compared to expected configuration in real-world deployment.