## Slide 1: Way forward on NR coexistence study for above 6GHz
China Telecom, China Unicom, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #82bis R4-1702869
Spokane, USA, 3 - 7 April, 2017

## Slide 2: Background
Contributions below provide the consideration on NR coexistence study for above 6GHz and suggest to do the further study in the WI.
  R4-1702867, Consideration on NR coexistence study for above 6GHz, China Telecom
  R4-1703546, Potential improvement of co-existence study in the WI phase, Huawei, HiSilicon
From the ACIR results in TR38.803, urban macro scenario is the worst case among the three simulation scenarios.

## Slide 3: WF on NR coexistence study for above 6GHz
The coexistence simulation for above 6GHz in urban macro scenario should be further investigated in the WI phase to align the simulation results and check if the the ACIR results for WP5D can be used in the WI.
All the companies provided results in the SI should apply the following simulation assumptions and provide the UL&DL coexistence results for urban macro scenario in the next meeting.
  The uncoordinated deployment should be considered
    The correlation of shadowing fading between base stations is 0.5.
    LOS/NLOS is assigned to each link independently with respect to different base stations.
    RAN4 should conclude co-existence study and fix the ACLR values by end of June meeting.