## Slide 1: Way forward on MPDCCH monitoring based requirements for feMTC
Nokia, Alcatel-Lucent Shanghai Bell, …
3GPP TSG-RAN WG4 Meeting #82bis
Spokane, US, April 3 – 7, 2017
Agenda: 7.18.3.2.1
R4-1703720

## Slide 2: Background
feMTC UE may be configured to monitor MPDCCH in a discontinuous manner.
Rel-13 eMTC UE RRM/RLM requirements are defined without considering MPDCCH monitoring configuration.
  UE power consumption may further benefit from taking the configurable MPDCCH monitoring into account

## Slide 3: WF on FeMTC requirements
RLM, RRM measurement requirements (including both intra- and inter-frequency) and ECID measurement requirements are updated to take UE MPDCCH monitoring configuration into account
  When UE is using DRX/eDRX:
    the existing Active state definition defined in 36.321 is followed; to be clarified in 36.133 that the current DRX/eDRX requirements apply, provided that the MPDCCH repetitions are configured in DRX ON
  When UE is not using DRX/eDRX:
    current non-DRX requirements apply, except:
      when G> 1, and
      r_max*G > MGRP for CEMode A and r_max*G>800ms for CEMode B
      when UE does not detect it is scheduled to receive data after the MPDCCH monitoring period
    In the above exceptions, the measurement period depends on r_max*G
SI reading requirements and OTDOA measurement requirements to be clarified that current requirements apply regardless of MPDCCH monitoring configuration
Interested companies are encouraged to provide CRs in RAN4#83.