## Slide 1: WF on UE and BS requirements in FDD L-band
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 #82bis Meeting Spokane, WA, USA, 3 - 7 April, 2017
R4-1704085

## Slide 2: Way forward
  For own Rx protection in 1475-1488 MHz,
    Two NSs will be specified for;
      Case 1) -30 dBm/MHz (general spurious emission level)
      Case 2) -25 dBm/MHz (condition which requires no A-MPR for 3 MHz CBW)
  Companies are encouraged to provide simulation results for both emission level in RAN4#83.
  The following simulations can be skipped.
    For case 1, 1.4 MHz CBW can be skipped since it’s obvious no A-MPR is needed based on the general spurious emission spec.
    For case 2, 1.4 and 3 MHz CBW can be skipped since it’s obvious no A-MPR is needed based on the SEM spec.
For the MSS protection for BS Tx, the treatment will be aligned with that of TDD and SDL.
  If specified, a note in the spec table should be modified not to mandate the guard-band.