## Slide 1: WF on BS IC receiver
China Telecom, ZTE, Nokia, Alcatel-Lucent Shanghai Bell, Huawei
3GPP TSG-RAN WG4 Meeting #82bis
Spokane, Washington, USA, April 3 - 7, 2017
R4-1704152

## Slide 2: Background
The BS IC link results without and with time and frequency offset are summarized in R4-1702819 and R4-1702820 respectively.
  For some cases, the span of different companies’ results is more than 2 dB (highlighted in yellow in the spreadsheet).
  By comparing the simulation results without and with time and frequency offset:
    2 companies observe that with robust channel estimation and demodulation algorithms against TO&FO, the performance degradation due to TO&FO is not obvious.
    1 company observes that 1-2dB loss when TO&FO is modeled but not handled.
There are 9 simulation cases for equal SNR and 13 cases for unequal SNR, and down-selection of the simulation case is needed.
According to the SID, the SI is scheduled to be complete in the next meeting.

## Slide 3: WF: Action points for the next meeting
On simulation results
  For cases with more than 2dB span, companies are invited to check and update the simulation results.
  More companies are invited to provide the simulation results with time and frequency offset.
Principle for down-selecting test case
  BS Rx number: cover 2Rx and 4Rx
  Propagation condition (intra-cell UEs, inter-cell UEs): cover (EPA5 low, ETU5 low), (EVA70 low, ETU70 low)
  Inter-cell interference scenario: cover high and/or low interference levels
  MCS: cover MCS 10/15
    MCS 21 could be considered if the motivation is justified
Test metric for performance requirements
  Option 1: SINR at 85% of maximum throughput of each individual intra-cell UE.
  Option 2: SINR at 85% of maximum sum throughput of all the intra-cell UEs.
  Option 3: SINR at 85% of maximum throughput of anyone of weakest intra-cell UE.
  Other options are not precluded.

## Slide 4: WF: Action points for the next meeting
Companies are invited to provide inputs on the aspects provided in the previous slide in the next meeting.
The test cases set in the following slides are just for information and provide some guideline on how the test cases would be down-selected based on the principle.

## Slide 5: For information: Possible test cases set
Option 1: select equal SNR cases
Case No. | Rx antenna | No. of UEs | Propagation condition (intra-cell UEs, inter-cell UEs) | MCS level (intra-cell UEs) | Inter-cell interference scenario
E1-a1 | 2 Rx | 2 UEs | (EPA5 low, ETU5 low) | MCS 10 | DIP1= -0.43 dB
E1-b1 |  |  | (EVA70 low, ETU70 low) | MCS 15 | DIP1 = -5.45 dB
E2-a1 | 4 Rx | 4 UEs | (EPA5 low, ETU5 low) | MCS 10 | DIP1= -0.43 dB
E2-b1 |  |  | (EVA70 low, ETU70 low) | MCS 15 | DIP1 = -5.45 dB

## Slide 6: For information: Possible test cases set
Option 1a: select equal SNR cases
Case No. | Rx antenna | No. of UEs | Propagation condition (intra-cell UEs, inter-cell UEs) | MCS level (intra-cell UEs) | Inter-cell interference scenario
E1-b2 | 2 Rx | 2 UEs | (EVA70 low, ETU70 low) | MCS 10 | DIP1= -5.45 dB
E1-c |  |  | (EPA5 low, ETU5 low) | MCS 21 | DIP1 = -0.43 dB
E2-a1 | 4 Rx | 4 UEs | (EPA5 low, ETU5 low) | MCS 10 | DIP1= -0.43 dB
E2-b1 |  |  | (EVA70 low, ETU70 low) | MCS 15 | DIP1 = -5.45 dB

## Slide 7: For information: Possible test cases set
Option 2: half of the cases with equal SNR + half of the cases with unequal SNR
Case No. | Rx antenna | No. of UEs | Propagation condition (intra-cell UEs, inter-cell UEs) | MCS level (intra-cell UEs) | Inter-cell interference scenario
E1-a1 | 2 Rx | 2 UEs | (EPA5 low, ETU5 low) | MCS 10 | DIP1= -0.43 dB
E2-a1 | 4 Rx | 4 UEs | (EPA5 low, ETU5 low) | MCS 10 | DIP1= -0.43 dB
U1-b1 | 2 Rx | 2 UEs | (EVA70 low, ETU70 low) | MCS 15 | DIP1 = -5.45 dB
U2-b1 | 4 Rx | 4 UEs | (EVA70 low, ETU70 low) | MCS 15 | DIP1 = -5.45 dB

## Slide 8: For information: Possible test cases set
Option 2a: half of the cases with equal SNR + half of the cases with unequal SNR
Case No. | Rx antenna | No. of UEs | Propagation condition (intra-cell UEs, inter-cell UEs) | MCS level (intra-cell UEs) | Inter-cell interference scenario
E1-a2 | 2 Rx | 2 UEs | (EPA5 low, ETU5 low) | MCS 15 | DIP1= -0.43 dB
E2-a1 | 4 Rx | 4 UEs | (EPA5 low, ETU5 low) | MCS 10 | DIP1= -0.43 dB
U1-c | 2 Rx | 2 UEs | (EPA5 low, ETU5 low) | MCS 21 | DIP1 = -0.43 dB
U2-b2 | 4 Rx | 4 UEs | (EVA70 low, ETU70 low) | MCS 10 | DIP1 = -5.45 dB

## Slide 9: For information: Possible test cases set
Option 3: half of the cases with equal SNR + half of the cases with unequal SNR
Case No. | Rx antenna | No. of UEs | Propagation condition (intra-cell UEs, inter-cell UEs) | MCS level (intra-cell UEs) | Inter-cell interference scenario
E1-b1 or E1-b2 | 2 Rx | 2 UEs | (EVA70 low, ETU70 low) | MCS 15 or MCS 10 | DIP1 = -5.45 dB
E2-b1 or E2-b2 | 4 Rx | 4 UEs | (EVA70 low, ETU70 low) | MCS 15 or MCS 10 | DIP1 = -5.45 dB
U1-d | 2 Rx | 2 UEs | (EPA5 low, ETU5 low) | MCS 10 for UE1 MCS 15 for UE2 | DIP1= -0.43 dB
U2-c | 4 Rx | 4 UEs | (EPA5 low, ETU5 low) | MCS 10 for UE1, 3 MCS 15 for UE2, 4 | DIP1= -0.43 dB

## Slide 10: For information: Possible test cases set
Option 4: select unequal SNR cases
Case No. | Rx antenna | No. of UEs | Propagation condition (intra-cell UEs, inter-cell UEs) | MCS level (intra-cell UEs) | Inter-cell interference scenario
U1-b1 or U1-b2 | 2 Rx | 2 UEs | (EVA70 low, ETU70 low) | MCS 15 or MCS 10 | DIP1 = -5.45 dB
U2-b1 or U2-b2 | 4 Rx | 4 UEs | (EVA70 low, ETU70 low) | MCS 15 or MCS 10 | DIP1 = -5.45 dB
U1-d | 2 Rx | 2 UEs | (EPA5 low, ETU5 low) | MCS 10 for UE1 MCS 15 for UE2 | DIP1= -0.43 dB
U2-c | 4 Rx | 4 UEs | (EPA5 low, ETU5 low) | MCS 10 for UE1, 3 MCS 15 for UE2, 4 | DIP1= -0.43 dB

## Slide 11: For information: Possible test case set
Option 5: half of the cases with equal SNR + half of the cases with unequal SNR
Case No. | Rx antenna | No. of UEs | Propagation condition (intra-cell UEs, inter-cell UEs) | MCS level (intra-cell UEs) | Inter-cell interference scenario
E1-a1 or E1-c | 2 Rx | 2 UEs | (EPA5 low, ETU5 low) | MCS 10 or 21 | DIP1 = -0.43 dB
E1-b1 | 2 Rx | 2 UEs | (EVA70 low, ETU70 low) | MCS 15 | DIP1 = -5.45 dB
U1-d | 2 Rx | 2 UEs | (EPA5 low, ETU5 low) | MCS 10 for UE1 MCS 15 for UE2 | DIP1= -0.43 dB
U2-c | 4 Rx | 4 UEs | (EPA5 low, ETU5 low) | MCS 10 for UE1, 3 MCS 15 for UE2, 4 | DIP1= -0.43 dB