## Slide 1: Way forward on the applicability of the demodulation requirements for UE supporting coverage enhancements
Ericsson, Intel, Qualcomm, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #82bis
Spokane, WA, USA, 3 - 7, February, 2017
R4-1704178

## Slide 2: Background
The Rel-13 Coverage Enhancement (CE) feature can be supported by any LTE UE category and not restricted to be used for Category M1 devices (i.e., BL/CE UEs) only.
Existing UE demodulation performance and CQI requirements for the CE feature are defined based on the simulation results with the Category M1 devices with single receive antenna
  It is not clear how to setup the test for demodulation and CQI requirements for devices with 2 and 4 receive antennas supporting CE
  The requirements for the devices with 2 and 4 receive antennas are not defined and existing Cat-M1 requirements may not be directly reused

## Slide 3: Way forward on coverage enhancement UE demodulation and CQI requirements for non-BL/CE UEs in Rel-13
Interested companies are encouraged to provide the preferable option for Rel-13 in RAN4#83 based on the analysis (e.g., UE implementation, RAN4 workload, etc.) and simulation results. (eMTC performance maintenance)
 | Antenna connection | Test setup and parameters | Requirements
Option 1-1 | Simplified antennas connection method (See appendix). The existing CE tests are performed by duplicating the fading channel from each Tx antenna and adding independent noise for each Rx antenna. | Same as Rel-13 eMTC except reduced SNR for CQI definition test | Same as Rel-13 eMTC.
Option 1-2 | Simplified antennas connection method (See appendix). The existing CE tests are performed by duplicating the fading channel from each Tx antenna and adding independent noise for each Rx antenna. | Same as Rel-13 eMTC except reduced SNR for CQI definition test | Add some margins to the Rel-13 requirements depending on the number of receive antennas
Option 2 | Full antenna connection method. New CE tests with full channel models are defined under assumption that channel fading is independently generated for each RX antenna. | Reuse the Rel-13 eMTC setting. Repetition number may be adjusted. | New requirements
Option 3 | Connect one antenna port regardless of the number of receive antennas. Rest of antenna ports are open or terminated. | Same as Rel-13 eMTC. | Same as Rel-13 eMTC.

## Slide 4: Way forward on coverage enhancement UE demodulation and CQI requirements for non-BL/CE UEs in Rel-14
RAN4 will discuss further the applicability of the Rel-13 coverage enhancement UE demodulation and CQI requirements to non-BL/CE UEs in Rel-14.
  Interested companies are welcome to provide the view on this issue in Rel-14 FeMTC performance.

## Slide 5: Appendix
Example of the simplified antenna connection for UE with 2 receive antennas (Ref: R4-1700875)