## Slide 1: Way forward on eFD-MIMO performance requirements
Samsung, Qualcomm, Ericsson, Intel, Huawei,CATT
3GPP TSG-RAN WG4 Meeting #82bis Spokane, US, 3 - 7 April, 2017
R4-1704205

## Slide 2
No BS performance requirements needed for Rel-14 eFD-MIMO WI
At least below UE performance test cases needed for Rel-14 eFD-MIMO WI
  New Class A PMI test cases
  New PDSCH demodulation test cases for semi-open MIMO transmission
  New PMI/RPI test case for advanced CSI codebook
  New CSI test case(s)for Hybrid CSI reporting mechanism
  PDSCH demodulation test case for AP ZP-CSI-RS transmission
  CSI test cases for Multi-shot CSI-RS and Aperiodic NZP CSI-RS
UE performance test cases will be introduced under 2Rx
UE performance test cases will be introduced under TM9 mode
Work scope

## Slide 3
Introduce two Class A PMI test cases in Rel-14 eFD-MIMO with different antenna ports:
  One test case for wideband PMI reporting
    Option 1: 28 port with CDM4
    Option 2: 24 port with CDM4
  One test case for sub-band PMI reporting
    32 port with CDM8
CSI-RS reduced density for non-precoded CSI-RS resources will be covered by Class A wideband PMI test case
  FFS test applicability
Pending on UE capability, random selection CSS configuration from UE supported list; and defining minimum performance requirements applicable for all CSS configurations.
Reusing test metric as Rel-13 Class A PMI test case as baseline
Class A PMI test cases

## Slide 4: MIMO correlation Matrix for Class A codebook
Reusing existing values for parameters α1, α2, β and γ for high spatial correlation as baseline, Further confirmed by companies’ simulation results
High spatial correlation |  |  | 
a1 | a2 | b | g
0.9 | 0.9 | 0.9 | 0.3
Note 1: Value of α1 applies when more than one pair of cross-polarized antenna elements in first dimension at eNB side. Note 2: Value of α2 applies when more than one pair of cross-polarized antenna elements in second dimension at eNB side. Note 3: Value of β applies when more than one pair of cross-polarized antenna elements at UE side. |  |  | 

## Slide 5
Test metric: existing test metric for PMI test case as relative throughput ratio under FRC as starting point: FFS for detailed random PMI approach
  Option1: randomize only {i1,3, i2, RPI}
  Option2: randomize {i1,1, i1,2,i1,3, i2, RPI}
  Other options not excluded
Introducing test case under rank2 transmission
Beam steering modelling:
  Option 1: introducing at least two cluster Beam direction with separate channel matrix
  Other options not precluded
PMI/RPI reporting test for the advanced CSI codebook

## Slide 6: PDSCH demodulation test cases for semi-open MIMO transmission
Introduce both Rank1 and rank2 test cases
FFS for :Beam-forming modeling
  Option 1: Using Random Beam-forming model
  Other options not excluded
Fading channel: EVA70Hz

## Slide 7: PDSCH performance test case for AP ZP-CSI-RS transmission
Based on one of existing test cases with Periodic ZP CSI-RS
  Replacing Periodic ZP CSI-RS as AP ZP CSI-RS
  Sub-frames for AP ZP-CSI-RS same as Periodic ZP CSI-RS SFs, the indicated AP ZP-CSI-RS configuration is random selected from RRC-configured AP ZP CSI-RS list
FFS for which existing test case can be used
FFS for applicability

## Slide 8: Simulation assumption for Class A PMI (Information Only)
Parameter | Unit | Test 1(Single PMI test) -28/24 ports | Test 2 (Multiple PMI test) -32 ports
Bandwidth | MHz | 10 | 10
Transmission mode |  | 9 | 9
Propagation channel |  | EPA5 | EVA5
Precoding granularity (only for reporting and following PMI) |  | 50 | 6
Correlation and antenna configuration |  | 2D High XP Option 1: 28 *2 Option 2: 24*2 | 2D High XP 32 x 2
Beamforming model |  | [Annex B.4.3] | [Annex B.4.3]
Cell-specific reference signals |  | Antenna ports 0,1 | Antenna ports 0,1
CSI reference signals |  | Antenna ports | Antenna ports
 |  | FFS | 15,…,46
Number of CSI-RS ports |  | Option 1: 28 Option 2: 24 | 32
CDM Type |  | CDM4 | CDM8
CSI-RS periodicity and subframe offset TCSI-RS / ICSI-RS |  | 5/1 | 5/1
NZP-CSI-RS-Configuration-List |  | FFS | {0,1,2,3}
FrequencyDensityNonPrecoded |  | FFS | 1
NZP-TransmissionCombNonprecoded |  | FFS | NA
eMIMO-Type |  | Class A | Class A
codebookConfig-N1 |  | FFS | FFS
codebookConfig-N2 |  | FFS | FFS
codebook-Over-Sampling-RateConfig-O1 |  | 8 | 8
codebook-Over-Sampling-RateConfig-O2 |  | 4 | 4
Codebook-Config |  | 1,2,3,4 | 1,2,3,4
codebookSubsetRestriction-1 |  | FFS | FFS
codebookSubsetRestriction-2 |  | FFS | FFS
Reporting mode |  | PUSCH 3-1 | PUSCH 1-2
Reporting interval | ms | 5 | 5
PMI delay | ms | 8 | 8
Measurement channel |  | FFS | FFS
Rank Number of PDSCH |  | FFS | FFS
Max number of HARQ transmissions |  | 4 | 4
Redundancy version coding sequence |  | {0,1,2,3} | {0,1,2,3}