## Slide 1: WF on lower and upper frequency limits and MBW for NR UE Tx spurious emission
ZTE Corporation
3GPP TSG-RAN WG4 Meeting #82bis | R4-1704408
Spokane, US, 3 - 7 April, 2017 Agenda item: 10.4.2.2 | 

## Slide 2: Background
In last meeting, the concept of frequency “Range 1 and Range 2” [1] has been introduced to specify RF requirements for NR. the threshold between frequency Range 1 and Range 2 hasn’t decided yet.
The upper and lower frequency limit and measurement bandwidth for NR are still incomplete although some conclusions have been captured into TR38.803[2][3].
For above 13 GHz transmission, it has been agreed that upper frequency limit should be specified as 2nd harmonics of the upper edge of the UL operating band including the full harmonic spectrum [2]
The upper limit will be very high (up to 200 GHz) if the NR frequency range is high according to ITU-R SM.329 [4]. For saving test time,1MHz measure bandwidth may be a little small for that much of high upper limit.[5]
[1] R4-1701520, Applicability of UE RF conducted and OTA requirements, NTT DOCOMO, INC.
[2] R4-1702045, TP for TR 38.803: SI agreements and background for each UE RF requirement. NTT DOCOMO, INC.
[3] R4-1702044, TP for TR 38.803: Summary of SI agreements on UE RF aspects, NTT DOCOMO, INC.
[4] Recommendation ITU-R SM.329-12, unwanted emissions in the spurious domain
[5] R4-1702847, NR UE Tx spurious emissions, ZTE, ZTE Microelectronics
[6] R4-1700864, NR UE Tx spurious emissions, ZTE, ZTE Microelectronics

## Slide 3: Way forward
For range 1
  Lower frequency limit
    9 KHz for below [6GHz]
  Upper frequency limit
    5th harmonic of the upper frequency edge of the UL operating band
  Measure bandwidth
    1 kHz between 9 kHz and 150 kHz
    10 kHz between 150kHz and 30 MHz
    100 kHz between 30 MHz and 1 GHz
    1MHz above 1 GHz
For range 2
  Lower frequency limit
    30 MHz for above [6GHz]
  Upper frequency limit
    2nd harmonic of the upper frequency edge of the UL operating band for above 13GHz
  Measure bandwidth
    100 kHz between 30 MHz and 1 GHz
    1 MHz above 1GHz
    Test time aspects should be further investigated