## Slide 1: WF on CRS-IM capability and assistance signalling
Qualcomm, Intel, CATT
3GPP TSG-RAN WG4 Meeting #83 Hangzhou, China., 15 - 19 May 2017
R4-1705128

## Slide 2: Background
Rel-13 CRS-IM capability signaling (crs-InterfMitigationTM1toTM9)
  Indicates whether the UE supports CRS interference mitigation (IM) while operating in the following transmission modes (TM): TM 1, TM 2, …, TM 8 and TM 9. The UE shall not include the field if it does not support CRS IM in TMs 1-9. If the field is present, the UE supports CRS-IM on at least one arbitrary downlink CC for up to crs-InterfMitigationTM1toTM9-r13 downlink CC CA configuration. The UE signals crs-InterfMitigationTM1toTM9-r13 value to indicate the maximum crs-InterfMitigationTM1toTM9-r13 downlink CC CA configuration where UE may apply CRS IM. For example, the UE sets “crs-InterfMitigationTM1toTM9-r13 = 3” to indicate that the UE supports CRS-IM on at least one DL CC for supported non-CA, 2DL CA and 3DL CA configurations. The UE supporting the crs-InterfMitigationTM1toTM9-r13 capability shall also support the crs-InterfHandl-r11 capability.
Rel-13 CRS assistance signaling
  eNB provide PCID, number of CRS ports and MBSFN subframe configuration for all neighbor potential neighbor cells
  CRS assistance signaling can be provided for both PCell and SCells.

## Slide 3: Background
Rel-14 Enhanced CRS-IM feature list
  #1: PDSCH non-colliding CRS-IM receiver for 2RX and 4 CRS APs
  #2: PDSCH non-colliding CRS-IM receiver for 4RX and 2 CRS APs
  #3: PDSCH non-colliding CRS-IM receiver for 4RX and 4 CRS APs
  #4: Type A CCIM receiver for 2RX and 4 CRS APs for DL Control Channels
  Other feature can be added depending on further RAN4 discussion
RAN4 need to define capability signaling that covers all CRS-IM features
It would be desirable to reduce CRS assistance signaling overhead

## Slide 4: WF on UE capability signaling
Option 1 : Define following per-UE capability signaling
  #1 CRS-IM capability
    UE can indicate per-UE CRS-IM capability if it supports at least one of features
      Rel-14 CRS-IM #1, #2, #3, #4
      Rel-13 CRS-IM
      Rel-14 CCIM
      on at least one CC in at least one CA configuration
  #2 CRS-IM + CRS port blind detection capability
    UE can indicate per-UE if it support neighboring cells CRS port blind detection on at least one CC in least one CA configuration
Option 2 : Define capability signaling in the same way as Rel-13 CRS-IM capability signaling for each feature
Other options are not precluded

## Slide 5: WF on CRS assistance signaling
Option 1: Introduce simplified CRS assistance signaling
Option 2: Keep Rel-13 CRS assistance signaling
Other options are not precluded

## Slide 6: Procedure with optimized CRS assistance signaling (information)
For UE with CRS-IM capability
  If network deployment is uniform (i.e. same CRS APs and MBSFN configurations across neighboring cells)
    1 bit flag to indicate that number of CRS ports in neighbor cells is same as serving cell
    1 bit flag to indicate that MBSFN SF configuration in neighbor cells is same as serving cell
  If network deployment is non-uniform (i.e. different CRS APs or MBSFN configurations across neighboring cells)
    Provide Rel-13 CRS assistance signaling for the neighboring cells and CCs which have different configurations from the Serving cell
    UE can assume that remaining neighboring cells have same configuration as serving cell
  CRS assistance signaling is provided per-CC

## Slide 7: Procedure with optimized CRS assistance signaling (information)
For UE with CRS-IM + CRS port blind detection capability
  If network deployment is uniform (i.e. same MBSFN configurations across neighboring cells)
    1 bit flag to indicate that MBSFN SF configuration in neighbor cells is same as serving cell
  If network deployment is non-uniform (i.e. different MBSFN configurations across neighboring cells)
    Provide Rel-13 CRS assistance signaling for the neighboring cells and CCs which have different configurations from the Serving cell
    UE can assume that remaining neighboring cells have same configuration as serving cell
  CRS assistance signaling is provided per-CC