## Slide 1: WF for test scenario for performance requirement for FeMBMS
Ericsson, Qualcomm
3GPP TSG-RAN WG4 Meeting #83 R4-1705368 Hangzhou, China, 15th-19th May, 2017
Document Type: Approval

## Slide 2: Channel model
It’s proposed for subcarrier spacing 15kHz and 7.5kHz tests the existing MBMS channel model could be reused. For subcarrier spacing 1.25kHz it’s proposed to define a new channel model as following.
Maximum Doppler frequency [5Hz] |  | 
Relative Delay [ns] |  | Relative Mean Power [dB] (1.25k/7.5k/15kHz numerology)
Extended Delay Spread [2] (7.5k/15kHz numerology) | Further Extended Delay Spread (1.25kHz numerology) | 
0 | 0 | 0
30 | 30 | -1.5
150 | 150 | -1.4
310 | 310 | -3.6
370 | 370 | -0.6
1090 | 1090 | -7.0
12490 | 49960 | -10
12520 | 49990 | -11.5
12640 | 50110 | -11.4
12800 | 50270 | -13.6
12860 | 50330 | -10.6
13580 | 51050 | -17.0
27490 | 109960 | -20
27520 | 109990 | -21.5
27640 | 110110 | -21.4
27800 | 110270 | -23.6
27860 | 110330 | -20.6
28580 | 111050 | -27.0

## Slide 3: Test proposals for PMCH demodulation
Define the following tests for mixed FeMBMS/unicast cell for PMCH demodulation
Cell type | Test number | Bandwidth | PMCH Reference Channel | MBSFN Subframe Subcarrier Spacing | Propagation condition | Correlation Matrix and antenna | Reference value |  | MBMS UE Category
 |  |  |  |  |  |  | BLER (%) | SNR(dB) | 
Pcell |  | 10 MHz | No PDSCH No PMCH | N/A | EPA5 | 1x2 low | N/A | N/A | 
FeMBMS SCell | 1 | 10 MHz | 16QAM 1/2 | 1.25 kHz | New MBSFN Channel w/ >100us delay spread | 1x2 low | 1 | TBD | ≥1
 | 2 | 10 MHz | 64QAM 2/3 | 1.25 kHz |  |  |  | TBD | ≥2
 | 3 | 10 MHz | 16QAM 1/2 | 7.5 kHz | MBSFN channel model (Table B.2.6-1) |  |  | TBD | ≥1
FeMBMS Non-Unicast reception Cell | 1a (Note 1) | 10 MHz | 16QAM 1/2 | 1.25 kHz | New MBSFN Channel w/ >100us delay spread | 1x2 low | 1 | TBD | ≥1
 | 2a (Note 1) | 10 MHz | 64QAM 2/3 | 1.25 kHz |  |  |  | TBD | ≥2
 | 3a (Note 1) | 10 MHz | 16QAM 1/2 | 7.5 kHz | MBSFN channel model (Table B.2.6-1) |  |  | TBD | ≥1
Note 1: Optional if UE are tested by tests of CA with Scell on the mixed FeMBMS/unicast carrier |  |  |  |  |  |  |  |  | 

## Slide 4: Test proposals for PMCH demodulation
Define the following tests for dedicated FeMBMS cell for PMCH demodulation
Cell type | Test number | Bandwidth | PMCH Reference Channel | MBSFN Subframe Subcarrier Spacing | Propagation condition | Correlation Matrix and antenna | Reference value |  | MBMS UE Category
 |  |  |  |  |  |  | BLER (%) | SNR(dB) | 
Pcell |  | 10 MHz | No PMCH, No PDSCH | N/A | EPA5 | 1x2 low | N/A | N/A | 
FeMBMS Non-Unicast reception Cell | 1 | 10 MHz | 16QAM 1/2 | 1.25 kHz | New MBSFN Channel w/ >100us delay spread | 1x2 low | 1 | TBD | ≥1
 | 2 | 10 MHz | 64QAM 2/3 | 1.25 kHz |  |  |  | TBD | ≥2
 | 3 | 10 MHz | 16QAM 1/2 | 7.5 kHz | MBSFN channel model (Table B.2.6-1) |  |  | TBD | ≥1
 | 4 (Note 1) | 10 MHz | 16QAM 1/2 | 15 kHz |  |  |  | TBD | ≥1
 | 5 (Note 1) | 5 MHz | 16QAM 1/2 | 15 kHz |  |  |  | TBD | ≥1
 | 6 (Note 1) | 3 MHz | QPSK 1/3 | 15 kHz |  |  |  | TBD | ≥1
Note 1: Optional if Ues are tested by PMCH reception from non-FeMBMS carrier |  |  |  |  |  |  |  |  | 

## Slide 5: Test proposal for PDSCH unicast demodulation
For unicast PDSCH demodulation test with MBSFN awareness, extend the existing single carrier single PRB allocation test 8.2.1.1.4 to the CA scenario with the increased MBSFN subframe allocation of 80%, where SCell is on the non-dedicated FeMBMS carrier.