## Slide 1: Way forward on eFD-MIMO performance requirements
Samsung, Qualcomm, Huawei, Ericsson, [CATT], [Intel]
3GPP TSG-RAN WG4 Meeting #83 Hangzhou, China, 15 - 19 May, 2017
R4-1706194

## Slide 2
No BS performance requirements for Rel-14 eFD-MIMO WI
Introducing below UE performance test cases for Rel-14 eFD-MIMO WI
  New Class A PMI test cases
  New PDSCH demodulation test cases for semi-open MIMO transmission
  New PMI/RPI test case for advanced CSI codebook
  New CSI test case for Hybrid CSI reporting mechanism2
  PDSCH demodulation test case for AP ZP-CSI-RS transmission
  CSI test cases for Multi-shot CSI-RS , Aperiodic NZP CSI-RS
  CSI test case for CSI-RS density reduction
FFS whether introducing CSI test case for Hybrid CSI mechanism 1
No need to introduce additional test for QCL behaviour B for multi-shot CSI-RS in Rel-14 eFD-MIMO WI.
No UE performance impact for UL DMRS enhancement.
Agreements

## Slide 3
Test 1 Single PMI test case : EPA5Hz, PUSCH 3-1 mode, CDM4, (O1,O2) = (8,4), (N1,N2) = (3,4)
  Antenna Ports:
    24 ports (N1,N2) = (3,4)
  Test 1-a: without CSI-RS density reduction
  Test 1-b: with CSI-RS density reduction
    d =1/3, Comb-offset list: {0,1,2}
  Pending on UE capability for supporting CSI-RS density reduction, pick up one of above test case to pass
Test 2 Multiple PMI test case(32 ports) : EVA5Hz, PUSCH 1-2 mode, CDM8, (O1,O2) = (8,4),(N1,N2) = (4,4), d=1
MCS and Rank
  Single PMI test case:
    Option1: 16QAM ½ Rank2
    Option2: 64QAM ½ Rank1
  Multiple PMI test case
    Option 1: 16QAM ½ Rank2
    Option 2: 64QAM ½ Rank2
Reusing existing values for parameters α1, α2, β and γ for high spatial correlation
Class A PMI test cases

## Slide 4: PDSCH demodulation test cases for semi-open MIMO transmission
Test parameters for Rank1 test case
  2*2 EVA[70Hz] with Medium correlation, QPSK 1/3
Test parameters for Rank2 test case
  16QAM , EVA [70Hz] , ULA low correlation
    Option 1: 4*2 MIMO
    Option 2: 2*2 MIMO
Precoding matrix
  Using precoding matrix following CSI calculation assumption as defined in RAN1 spec with single-stage codebook without PMI feedback during test
  2Tx: 1/sqrt(2) [1 0;0 1];
  4Tx:

## Slide 5
Test metric: existing test metric for PMI test case as relative throughput ratio under FRC as starting point:
    Randomize only {i1,3, i2, RPI}
Introduce advanced Codebook PMI test case with below configuration:
    PUSCH 1-2 feedback mode, 16 CSI-RS ports with (N1,N2) = (2,4), (O1, O2) = (8, 4), CDM4, CSS configuration = 1,2, 3, 4 , EVA5Hz, with Rank2 transmission
  FFS for beam steering method
    Option 1: multi-cluster beam steering
    Other options not excluded
PMI/RPI reporting test for the advanced CSI codebook

## Slide 6: PDSCH performance test case for AP ZP-CSI-RS transmission
Introducing new PDSCH demodulation test for AP ZP-CSI-RS by replacing the periodic ZP CSI-RS configuration in the existing PDSCH demodulation test with the equivalent aperiodic ZP CSI-RS.
  Reusing test parameter of Test 1 specified in table 8.3.1.1-1 and Table 8.3.1.1-2 of TS 36.101
  Sub-frames for AP ZP-CSI-RS same as Periodic ZP CSI-RS SFs, the indicated AP ZP-CSI-RS configuration is random selected from RRC-configured AP ZP CSI-RS list
  ZP CSI-RS configuration list (FDD)
    State 0: 0001000000000000
    State 1: 0100000000000000

## Slide 7: CSI Test cases for Multi-Shot and Aperiodic CSI-RS
Introduce new CSI test case for “multi-shot” CSI-RS mechanism based on existing Class B K=1 PMI test case
  Two NZP CSI-RS resources are configured, and one of the two CSI-RS resources is activated in the alternating way when measuring Tue .
Introduce new CSI test case for aperiodic CSI-RS mechanism based on existing Class B K=1 PMI test case
  Two NZP CSI-RS resources are configured and activated at the same time when measuring Tue , and TE randomly selects one of the two CSI-RS resource at each aperiodic CSI-RS transmission. In case UE supports only Nmax = 1, only one CSI-RS resource is activated and used.

## Slide 8: CSI Test cases for Class B CSI-RS density reduction
Introduce CSI test case for CSI-RS density reduction based on existing Class B K=1 PMI test case
  Pending on UE capability for supporting CSI-RS density reduction , either pass existing Class B K=1 PMI test case or new test case with CSI-RS density reduction