## Slide 1: WF on FeMBMS RRM
Ericsson, Qualcomm, Nokia, Alcatel-Lucent Shanghai Bell
3GPP TSG-RAN WG4 Meeting #83 R4-1706012
Hangzhou, China, 15 – 19 May 2017

## Slide 2: General
Clarify that numerology switching between MBSFN and non-MBSFN subframe does not cause interruption to UE unicast operation
Clarify that numerology switching between MBSFN and non-MBSFN subframe does not cause delay to UE unicast operation
Based on UE capabilities, for UE in RRC_CONNECTED with LTE PCell
  An FeMBMS/unicast-mixed cell is:
    Intra-frequency candidate Scell (included in max 8 intra-frequency cells), or
    inter-frequency candidate SCell (included in max 4 inter-frequency cells over 3 inter-frequency carriers), or
    Deactivated or activated Scell (included in supported band combinations)

## Slide 3: FeMBMS/Unicast-mixed carrier
Introduce intra-frequency, inter-frequency, and SCC requirements
Inter-frequency requirements are to be defined based on the assumption that subframes #0 and #5 are available for unicast measurements

## Slide 4: MBSFN measurement
  MBSFN RSRP unit is given by dBm/1.25kHz and dBm/7.5kHz for 1.25 kHz and 7.5 kHz numerology respectively in the new mapping tables, if the new mapping tables are agreed. And if the changes were agreed, RAN4 should inform RAN2
  RAN4 clarify the existing MBSFN RSRP/RSRQ requirements can be reused at least under the assumption that
    MBSFN RSRP|dBm/(L)kHz = MBSFN RSRP|dBm/15kHz + 10∙log10(L/15), L (=1.25, 7.5, 15)