## Slide 1: WF on RF requirements for microcell and picocell NB-IoT BS
Nokia, Nokia Shanghai Bell, Ericsson, Huawei
3GPP TSG-RAN WG4 Meeting #84 Berlin, Germany, 21 - 25 August, 2017
Agenda Item: 8.24.2.1
R4-1708809

## Slide 2: Background
Contributions on RF requirements for microcell and picocell NB-IoT BS have been discussed in RAN4#84:
  [1] R4-1707147 Transmitter requirements for picocell NB-IoT BS Nokia, Nokia Shanghai Bell
  [2] R4-1707148 Receiver requirements for microcell NB-IoT BS Nokia, Nokia Shanghai Bell
  [3] R4-1707149 Receiver requirements for picocell NB-IoT BS Nokia, Nokia Shanghai Bell
  [4] R4-1707647 BS RF requirements impacts analysis Ericsson
  [5] R4-1708131 Transmitter requirements for NB-IoT small cell Huawei, Hisilicon
  [6] R4-1708132 Receiver requirements for NB-IoT Pico cell Huawei, Hisilicon
Many proposals are aligned with each other.

## Slide 3: Way forward on microcell BS TX requirements
To apply the medium range E-UTRA or MSR BS output power and accuracy requirements also to the medium range NB-IoT BS.
To adopt the wide area NB-IoT BS output power dynamics requirements (including NB-IoT RB power dynamic range for in-band or guard band operation) to the medium range NB-IoT BS.
To apply the medium range E-UTRA BS frequency error requirement also to the medium range NB-IoT BS.
To adopt the wide area NB-IoT BS EVM, TAE and DL RS power requirements to the medium range NB-IoT BS.
To adopt the wide area NB-IoT BS occupied bandwidth and relative ACLR requirements to the medium range NB-IoT BS.
To apply the absolute ACLR limit for the medium range E-UTRA or MSR BS also to the medium range NB-IoT BS.
To apply the medium range E-UTRA or MSR BS operating band unwanted emissions requirements also to the medium range NB-IoT BS for in-band and/or guard band operations.
To use the same -91 dBm/100 kHz emission limit as the medium range E-UTRA or MSR BS for the medium range NB-IoT BS for protection of own BS receiver and co-location with other BS.
To adopt the wide area NB-IoT BS mandatory spurious emission limits and requirements for co-existence with systems operating in other frequency bands to the medium range NB-IoT BS.
To adopt the wide area NB-IoT BS transmitter intermodulation requirement to the medium range NB-IoT BS.

## Slide 4: Way forward on picocell BS TX requirements
To apply the local area E-UTRA or MSR BS output power and accuracy requirements also to the local area NB-IoT BS.
To adopt the wide area NB-IoT BS output power dynamics requirements (including NB-IoT RB power dynamic range for in-band or guard band operation) to the local area NB-IoT BS.
To apply the local area E-UTRA BS frequency error requirement also to the local area NB-IoT BS.
To adopt the wide area NB-IoT BS EVM, TAE and DL RS power requirements to the local area NB-IoT BS.
To adopt the wide area NB-IoT BS occupied bandwidth and relative ACLR requirements to the local area NB-IoT BS.
To apply the absolute ACLR limit for the local area E-UTRA or MSR BS also to the local area NB-IoT BS.
To apply the local area E-UTRA or MSR BS operating band unwanted emissions requirements also to the local area NB-IoT BS for in-band and/or guard band operations.
To use the same -88 dBm/100 kHz emission limit as the local area E-UTRA or MSR BS for the local area NB-IoT BS for protection of own BS receiver and co-location with other BS.
To adopt the wide area NB-IoT BS mandatory spurious emission limits and requirements for co-existence with systems operating in other frequency bands to the local area NB-IoT BS.
To adopt the wide area NB-IoT BS transmitter intermodulation requirement to the local area NB-IoT BS.

## Slide 5: Way forward on microcell BS RX requirements
To specify the in-channel selectivity requirement of medium range NB-IoT BS for in-band operation with the wanted and interfering signals increased by 5 dB comparing to the wide area NB-IoT BS for in-band operation.
To specify the narrow-band blocking requirement of medium range NB-IoT BS with the wanted and interfering signals increased by 5 dB comparing to the wide area NB-IoT BS.
To specify the same out-of-band blocking requirement as the wide area NB-IoT BS for the medium range NB-IoT BS.
To use the same +8 dBm interfering signal power level as the medium range E-UTRA or MSR BS for the medium range NB-IoT BS co-location blocking requirement.
To apply the wide area NB-IoT BS receiver spurious emissions requirement also to medium range NB-IoT BS.
To specify the receiver intermodulation requirement of medium range NB-IoT BS with the wanted and interfering signals increased by 5 dB comparing to the wide area NB-IoT BS, and the offsets between the interfering signal centre frequencies and the nominal band edge of the wanted carrier can also be reused.
To specify the receiver narrowband intermodulation requirement of medium range NB-IoT BS with the wanted and interfering signals increased by 5 dB comparing to the wide area NB-IoT BS, and the offsets between the interfering signal centre frequencies and the nominal band edge of the wanted carrier can also be reused.

## Slide 6: Way forward on picocell BS RX requirements
To specify the reference sensitivity requirement of local area NB-IoT BS with 8 dB relaxation comparing to the wide area NB-IoT BS.
To specify the dynamic range requirement of local area NB-IoT BS with the wanted and interfering signals increased by 8 dB comparing to the wide area NB-IoT BS.
To specify the in-channel selectivity requirement of local area NB-IoT BS for in-band operation with the wanted and interfering signals increased by 8 dB comparing to the wide area NB-IoT BS for in-band operation.
To specify the ACS requirement of local area NB-IoT BS with the wanted and interfering signals increased by 8 dB comparing to the wide area NB-IoT BS.
To specify the narrow-band blocking requirement of local area NB-IoT BS with the wanted and interfering signals increased by 8 dB comparing to the wide area NB-IoT BS.
To specify the in-band blocking requirement of local area NB-IoT BS with the wanted and interfering signals increased by 8 dB comparing to the wide area NB-IoT BS.
To specify the same out-of-band blocking requirement as the wide area NB-IoT BS for the local area NB-IoT BS.
To use the same -6 dBm interfering signal power level as the local area E-UTRA or MSR BS for the local area NB-IoT BS co-location blocking requirement.
To apply the wide area NB-IoT BS receiver spurious emissions requirement also to local area NB-IoT BS.
To specify the receiver intermodulation requirement of local area NB-IoT BS with the wanted and interfering signals increased by 8 dB comparing to the wide area NB-IoT BS, and the offsets between the interfering signal centre frequencies and the nominal band edge of the wanted carrier can also be reused.
To specify the receiver narrowband intermodulation requirement of local area NB-IoT BS with the wanted and interfering signals increased by 8 dB comparing to the wide area NB-IoT BS, and the offsets between the interfering signal centre frequencies and the nominal band edge of the wanted carrier can also be reused.

## Slide 7: FFS on Operating Band Unwanted Emission
Whether to apply the medium range MSR with GSM/EDGE BS operating band unwanted emissions requirements also to the medium range NB-IoT BS for standalone operations, or to apply the wide area NB-IoT BS operating band unwanted emissions requirements with power scaling.
Whether to apply the local area MSR with GSM/EDGE BS operating band unwanted emissions requirements also to the local area NB-IoT BS for standalone operations, or to apply the wide area NB-IoT BS operating band unwanted emissions requirements with power scaling.