## Slide 1: WF for dynamic transient period and Teval window for power control
Qualcomm, Ericsson, Huawei
3GPP TSG-RAN WG4 RAN4 #84
Berlin, Germany, 27th-29th, 2017
R4-1708903
Document for: Approval

## Slide 2: Background 1/2
In [1-5], various proposals to determine the location of the transient period have been proposed.
Since the number of cases is large, companies are requested to propose a simpler equation or logic to determine the transient period for all the use cases listed in [1-5]

## Slide 3: Background 2/2
In [6-7], discuss Teval and Tref window for determining PCmax computation
During offline discussions, it is agreed that frequency hopping duration needs to be considered in the Teval window to be consistent with that of 1msec TTI

## Slide 4: Agreements
Transient time for:
  ON_to_OFF and OFF_to_ON: 10 usec
  Two consecutive sTTIs: 10+10 usec
  For sTTI+SRS: 10+10 usec.

## Slide 5: Agreement on dynamic transient period
A simple logic is required to determine the location of the transient period without degrading system performances still.
Following logic has been agreed for consecutive sTTI w/wo SRS is:
  If the symbol on the right of the transient is ‘R’:
    Then irrespective of the symbol on the left, place the transient in the right ‘R’
  Else if the symbol left of the transient is ‘R’:
    Then irrespective of the symbol on the right, place the transient in left ‘R’
  Else:
    Share the transient symmetrically between the symbols.
This logic would be checked for consecutive 1msec+2osTTI and 1msec and 7os TTI

## Slide 6: Agreement
Pcmax evaluation for single carrier:
  Teval window should consider frequency hopping duration to be consistent with that of 1msec TTI
Where “Frequency-Hopping-Duration” is defined as the minimum duration of consecutive symbols without frequency hopping.
TTI duration | TREF | Teval
14 OS (1 ms) | 1 subframe | 1 slot
2 OS | 2 OS | Min(“Frequency-Hopping-Duration”, 2os)
7 OS | 7 OS | Min(“Frequency-Hopping-Duration”, 7os)

## Slide 7: References
R4-1707649, UE ON-OFF masks,
R4-1707977, UE ON/OFF time mask for all use cases
R4-1707793, Transient period and its location in the presence of SRS
R4-1707797, Case for a new data pattern for 2os TTI
R4-1707762, Transient period for ON-OFF and between two sTTI transmissions
R4-1707763, PCmax TREF and Teval window for sTTI
R4-1708151, UL power control with shortened TTI patterns for single carrier operation