## Slide 1: WF on power class and CDF
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 NR#84 Meeting
Berlin, Germany, 21st – 25th August, 2017
R4-1708914

## Slide 2: Background
In LTE, Power class (conducted) is referred in PCMAX formula
In NR mmW, power class definition and CDF have been discussed in RAN4, and it was agreed to define power class based on EIRP
How to reflect the EIRP based power class into TS 38.101 needs to be clarified

## Slide 3: WF on CDF and power class
To send an LS to ask if RAN1 assumes independent power control for beam and power changes due to beam changes
To agree Power class definition in next meeting considering below candidates according to the possible RAN1 answer
  Peak EIRP over the sphere with minus tolerance
  EIRP at CDF percentiles with minus tolerance
    [5-20] %
    [50] %
    [80-90] %
  Maximum allowed EIRP such as 43, 55 dBm (FCC limits)
Maximum allowed TRP will be discussed in the next meeting
Interested companies shall provide input on feasible values for the above mentioned parameters to next meeting

## Slide 4: WF on format
  CDF EIRP studies will be provided based on the above format to determine the final EIRP requirement
Meas. or Sim. |  | 
frequency range |  | 
antenna type |  | 
Pout per element | dBm | 
# of antenna in an array |  | 
# of arrays in the UE |  | 
# of measurement point |  | 
array gain | dB | 
element gain | dB | 
polarization Gain | dB | 
diversity gain | dB | 
Frequency Variation | dB | 
Implementation margin | dB | 
Case Losses (not include beam pointing loss) | dB | 
TRP | dBm | 21 dBm for calibration purpose
TRP Tolerance (+) | dB | 
5 %CDF | dBm | 
10 %CDF | dBm | 
20 %CDF | dBm | 
50 %CDF | dBm | 
80 %CDF | dBm | 
90 %CDF | dBm | 
Peak EIRP over the sphere | dBm | 
EIRP Tolerance (-) | dB | 
*Note: Minimum EIRP over the sphere can also be provided

## Slide 5: Reference
R4-1707331 UE Power class for mmWave 28GHz Sony
R4-1707509 PCMAX in mmWave OTA NTT DOCOMO, INC.
R4-1707700 NR Power Class Definition for cmW and mmW range InterDigital, Inc.
R4-1707794 Verification of Pcmax and UL power control for mmW Ericsson
R4-1707816 On mmW UE EIRP CDF MediaTek (Chengdu) Inc.
R4-1707818 mmW UE power class MediaTek (Chengdu) Inc.
R4-1707823 mmWave power class definition Huawei, HiSilicon
R4-1707825 Preliminary smartphone EIRP performance evaluation Huawei, HiSilicon
R4-1708127 Power class definition of different mmWave UE types Sumitomo Elec. Industries, Ltd
R4-1708143 Power class definition of mmWave UE Sumitomo Elec. Industries, Ltd
R4-1708162 NR UE power class for mmWave UE LG Electronics France
R4-1708609 mmW Output Power Qualcomm Incorporated
R4-1708618 UE Power Class for mm-wave Intel Corporation