## Slide 1: WF on UE capability signaling for LTE-NR DC Band Combination
Intel Corporation, Huawei, Apple, HiSilicon, vivo, OPPO
3GPP TSG-RAN WG4 RAN4 #84
Berlin, Germany, 27th-29th August, 2017
R4-1708944
Document for: Approval

## Slide 2: Background
Simultaneous LTE-NR UL transmission has potential coexistences problems and it has been identified as critical impact on receiver performance in certain bands and CA combinations.
RAN1 agreed to allow a single UL Tx [R1-1714827]
  Working assumption:
  When the UE is configured with multiple UL carriers on different frequencies (where there is at least one LTE carrier and at least one NR carrier of a different carrier frequency), but the UE operates on only one of the carriers at a given time among a pair of LTE and NR carriers
  UE can be configured with
    Case 1: DL-reference UL/DL configuration defined for LTE-FDD-SCell in LTE-TDD-FDD CA with LTE-TDD-PCell
      For scheduling/HARQ timing of LTE FDD carrier, DL-reference UL/DL configuration defined for LTE-FDD-SCell in LTE-TDD-FDD CA with LTE-TDD-PCell is applied
      UE is allowed to transmit NR UL signals at least in the subframe(s) where LTE UL transmission is not allowed according to the DL-reference UL/DL configuration
    Case 2: Release 15 LTE-FDD HARQ timing
      No impact on LTE RAN1 specifications
    Note: it doesn’t necessarily imply that UE has to support both cases
  To be confirmed this week (if no concerns raised by Friday noon time, it will be automatically confirmed)
For those issue expected band and CA combo, UE should have a flexibility to transmit single UL transmission.

## Slide 3: Proposal
It is proposed to introduce band combination specific UE capability signaling to indicate single UL Tx or 2 UL Tx support for LTE-NR DC.
Support for 2 UL Tx at the simultaneous time is optional for UE for each LTE-NR DC band combination

## Slide 4: Reference
R4-1704759, “Co-existence analysis on LTE-NR band combinations” Samsung