## Slide 1: WF on system acquisition time reduction for BL/CE UEs
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #84 R4-1709048
Berlin, Germany, 21th – 25th August, 2017
Agenda Item: 8.25.3.2

## Slide 2: Background (1)
RAN1#88bis and RAN1#89 made the following agreements regarding system acquisition time reduction for BL/CE UEs in Rel-15 [1]
Techniques for system acquisition time reduction to be considered:
  PSS/SSS
    Enhanced (e.g. repeated) PSS/SSS based on PSS/SSS or NPSS/NSSS design
    Use of NPSS/NSSS on NB-IoT anchor carrier
  PBCH
    Enhanced (e.g. repeated) PBCH based on PBCH or NPBCH design
    Use of NPBCH on NB-IoT anchor carrier
    Combining across 40-ms PBCH periods (unless already part of Rel-14 demodulation requirements)
    New mechanism allowing to skip MIB message reading
  SIB1-BR
    Additional repetitions of SIB1-BR
    Accumulation across SIB1-BR modification periods (unless already part of Rel-14 demodulation requirements)
    New mechanism allowing to skip SIB1-BR reading
      E.g. SI update indication or other indication in MIB or another channel
  SI messages
    Additional repetitions of SI messages
    Accumulation across SI modification periods
    New mechanism allowing to skip SI message reading
      E.g. SI update indication or other indication in MIB or another channel

## Slide 3: Background (2)
Among techniques in the LS for system acquisition time reduction to be considered by RAN1, only mechanism allowing to skip MIB message reading (sameSFN-indication) is completed in Rel-14.

## Slide 4: Proposal:
RAN4 shall wait RAN1 progress on system acquisition time reduction.
Add application rule to reuse Rel-14 FeMTC handover delay requirement for Rel-15 eFeMTC.