## Slide 1
Way forward on spectrum utilization
Samsung, Qualcomm, Intel, Ericsson, Nokia,[ZTE]
3GPP TSG-RAN WG4 #84
Berlin, Germany, 21st – 25th August, 2017
Agenda: 9.3.3
R4-1709075

## Slide 2: Background: Previous agreement
SCS [kHz] | 5MHz | 10MHz | 15MHz | 20 MHz | 25 MHz | 40 MHz | 50MHz | 60 MHz | 80 MHz | 100 MHz
 | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB
15 | 25 | 52 | [79] | [106] | [133,135] | [216] | 270 | N.A | N.A | N.A
30 | [11] | [24] | [38] | [51,52] | [65] | [106] | 133 | [162] | [217] | [273]
60 | N.A | [11, 12] | [18] | [24] | [31, 32] | [51, 52] | [65] | [79] | [107] | [135]
SCS [kHz] | 50MHz | 100MHz | 150MHz | 200 MHz | 400 MHz
 | NRB | NRB | NRB | NRB | NRB
60 | [66-67] | [132-136] | [198-204] | [264-275] | N.A
120 | [32] | [66-67] | [98-102] | [132-137] | [264-275]

## Slide 3: WF on spectral utilization for below 6GHz
SCS [kHz] | 5MHz | 10MHz | 15MHz | 20 MHz | 25 MHz | 40 MHz | 50MHz | 60 MHz | 80 MHz | 100 MHz
 | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB
15 | 25 | 52 | 79 | 106 | 133 | 216 | 270 | N.A | N.A | N.A
30 | 11 | 24 | 38 | 51 | 65 | 106 | 133 | 162 | 217 | 273
60 | N.A | 11 | 18 | 24 | 31 | 51 | 65 | 79 | 107 | 135
Above RB values are agreed based on the assumption of symmetric guard band.
The RB values in the table are only meant to indicate the minimum guard band achievable for a given SCS and channel BW . The actual maximum RB allocation can be equal to or 1 RB less than the values shown in the table.
Note1: Above RB values are agreed based on the assumptions of below requirements for sub 6GHz:
BS requirements: output power limit (R4-1706960), ALCR/ACS requirements (R4-1706971),EVM requirements (R4-1706969)
,SEM requirements (R4-1706973);
UE requirements: Power Class (PC3 and PC2), ALCR/ACS requirements (R4-1706525),EVM requirements (R4-1706612),SEM requirements; (R4-1706692)
Companies can further check above RB values based on further agreements for above requirements and agreements for channel raster.
Above RB values are agreed based on the assumption of no edge PRB EVM requirements in Rel-15.
Note2: Above RB values are derived based on RAN4 perspective, which can be further check by other working groups i.e. sub-carrier and RB alignment, and RB allocation restriction for DFT-OFDM waveform

## Slide 4: WF on spectral utilization for mmWave
Note 1: Above RB values are agreed based on the assumption of symmetric guard band. If asymmetric guard-band agreed, potential 1 RB reduced may be considered.
The RB values in the table are only meant to indicate the minimum guard band achievable for a given SCS and channel BW. The actual maximum RB allocation can be equal to or 1 RB less than the values shown in the table.
Note1: Above RB values are agreed based on the assumptions of below requirements for mm Wave:
BS requirements: output power limit (R4-1706960), ALCR/ACS requirements (R4-1706954),SEM requirements (R4-1706964);
UE requirements: Power Class definition (R4-1706945), ALCR/ACS requirements (R4-1706063), SEM requirements (R4-1706073);
Companies can further check and bring analysis for above RB values based on further agreements for above requirements and agreements for channel raster, BS EVM and UE EVM requirements.
Above RB values are agreed based on the assumption of no edge PRB EVM requirements in Rel-15.
Note2: Above RB values are derived based on RAN4 perspective, which can be further check by other working groups i.e. sub-carrier and RB alignment, and RB allocation restriction for DFT-OFDM waveform
SCS [kHz] | 50MHz | 100MHz | 200MHz | 400 MHz
 | NRB | NRB | NRB | NRB
60 | 66 | 132 | 264 | N.A
120 | 32 | 66 | 132 | 264