## Slide 1: WF on NR Mixed Numerologies FDM Requirements
Intel Corporation
3GPP TSG-RAN WG4 Meeting #84
Berlin, Germany, 21 - 25 August 2017
Agenda Item: 9.3.4
R4-1709076

## Slide 2: Background
Mixed Numerologies FDM operation use cases
  Use Case #1: Data and Data mixed numerology FDM
    FDM’ed transmission or reception of physical channels (e.g. NR PDSCH, PDCCH, PUSCH, PUCCH) with different numerologies at the same instance in DL or UL
  Use Case #2: Data and SS block (SS, PBCH) mixed numerology FDM
    FDM’ed transmission or reception of SS block (SS/PBCH) and other physical channels (e.g. NR PDSCH, PDCCH) with different numerologies in DL
Previous agreements are captured in R4-1706963

## Slide 3: Way Forward
Case 2 Data/SS mixed numerology FDM operation
  Data/SS mixed numerology FDM operation can be supported for both BS/UE without additional in-band RF requirements compared to single numerology.
  Do not define dedicated BS and UE in-band RF requirements in Rel-15 related to Data/SS mixed numerology FDM .
  Support of simultaneous reception of Data/SS with mixed numerologies is optional from UE implementation perspective
  RAN4 will investigate further how UE RRM requirements will take this into account
    Case 1: Intra-frequency cell identification and measurements on the target cell while receiving Data from the serving cell with different numerology from SS
    Other cases are not precluded