## Slide 1: WF on beam switching time
NTT DOCOMO, INC.
R4-1709079
3GPP TSG-RAN WG4 Meeting #84
Berlin, Germany, 21-25 August 2017
Agenda Item: 9.5.2.1

## Slide 2: Background
Base on the agreed WF in the last meeting [R4-1706957], Beam switching speed as NR BS new requirements are discussed in [1-8].
This contribution summarizes way forward/agreement on this topic.
[1] R4-1707491 Discussion on beam switching transient period for NR CATT
[2] R4-1707560 Proposal on NR BS beam switching speed requirements NTT DOCOMO, INC.
[3] R4-1707733 Impact of Beam Switching Ericsson
[4] R4-1707964 Discussion on beam switching speed for NR BS ZTE Corporation
[5] R4-1708078 Consideration on Beam Switching Speed Nokia, Nokia Shanghai Bell
[6] R4-1708108 On beam switching new requirement Ericsson
[7] R4-1708423 Discussion on Beam switching time Huawei

## Slide 3: Agreement (General)
Testability doesn’t impact the decision whether this requirement is introduced in core spec or not. (already agreed in R4-1706158)
RAN4 agrees to work to create a description for the potential requirement. (already agreed in R4-1706158)
RAN4 agrees the switching time must be less than some value (it doesn’t mean RAN4 automatically to introduce the requirement)
It is agreed RAN4 to encourage to solve remaining open issues shown in the following slides.

## Slide 4: Agreement (the value)
Taking into account NR OFDM symbol design, beam switching time of direction A to B shall be at least less than CP length
  CP length depends on SCS.
  The difference of direction A and B should be the same with the maximum direction gap which BS can steer.
Encouraged companies provide the simulation results of the relation between beam switching time (0 ~ CP length) and performance degradation (100% is assumed for no delay) for each DL CH in RAN4 NR#3 meeting in Nagoya and RAN4#84bis in Dubrovnik. Based on the results, RAN4 will further clarify the required beam switching time smaller than CP length.
FFS how beam switching and the time requirement should be defined in requirement text
Information | 
SCS | CP length
15 kHz | 4.69 µs
30 kHz | 2.34 µs
60 kHz | 1.17 µs
120 kHz | 586 ns
240 kHz | 293 ns

## Slide 5: Agreement (on Work Plan)
RAN4(month) | Core spec drafting | Beam switching time | Metric to be used | Testing feasibility
#84(Aug.) | This WF. |  |  | 
NR#3(Sep.) | (Provide draft) | Provide results | Agree some options, summarize Pros/Cons | Provide candidate testing method
#84bis(Oct.) | Update draft | Provide results | Continue and agree the metric | Continue and summarize the options
NR#4(Oct.-Nov.) | Agree the potential spec description other than value and metric | Provide results and decide the value | Agree the metric | Continue
#85(Nov.) | Agree the TP for TR | - | - | Clarify the test ability on each
NR #4(Jan.) |  |  |  | Decide possible test method(s)
#86(Feb.) |  |  |  | Provide draft spec
#86bis(Apr.) |  |  |  | Provide draft spec and conclude test feasibility
#87(May) |  |  |  | Agree the TP for TR